Automatic Scaling of Critical Frequency foF2 from 
Ionograms Recorded at São José dos Campos, Brazil: 
A Comparison Between Autoscala and UDIDA Tools

Michael PEZZOPANE1, Valdir Gil PILLAT2, 
and Paulo Roberto FAGUNDES2

1Istituto Nazionale di Geofisica e Vulcanologia, Rome, Italy; 
e-mail: michael.pezzopane@ingv.it

2Laboratório de Física e Astronomia, Universidade do Vale do Paraíba (UNIVAP), São José dos Campos, São Paulo, Brazil; 
e-mails: valdirgp@univap.br, fagundes@univap.br

Abstract

This paper considers a dataset of ionograms recorded by the CADI ionosonde installed at São José dos Campos (SJC; 23.2°S, 45.9°W, magnetic latitude 14.1°S), Brazil, to compare two autoscaling systems: Autoscala, developed by the Istituto Nazionale di Geofisica e Vulcanologia, and the UDIDA-scaling, developed by the Universidade do Vale do Paraíba. The analysis, focused on the critical frequency of the F2 layer, foF2, shows that the two systems work differently. The UDIDA-scaling gives always a value of foF2 as output, regardless of the presence of the ionogram trace and its definition, while Autoscala tends to reject ionograms for which the digital information is considered insufficient. As a consequence, the UDIDA-scaling can autoscale more foF2 values than Autoscala, but Autoscala can discard a larger number of ionograms for which the trace is unidentifiable. Discussions are made on the accuracy of the foF2 values given as output, as well as on the main shortcomings characterizing the two systems.

Key words: ionogram, ionosonde, low-latitude ionosphere, critical frequency foF2, automatic scaling.

INTRODUCTION

The importance of recording real time vertical sounding data, especially for space weather purposes, has greatly increased over the past years. In particular, the assimilation of this kind of data into ionospheric models has become more and more important (Pezzopane et al. 2011, 2013; Galkin et al. 2012, Lee et al. 2012, McNamara et al. 2013, Gardner et al. 2014, Chartier et al. 2016, Sabbagh et al. 2016). For this reason, in the last decades, several groups of researchers worked hard to implement systems able to automatically scale the experimental trace obtained after performing an ionospheric vertical sounding, that is, an ionogram (Reinisch and Huang 1983, Fox and Blundell 1989, Igi et al. 1993, Tsai and Berkey 2000, Zabotin et al. 2006, Ding et al. 2007, Galkin and Reinisch 2008, Su et al. 2012, Chen et al. 2013, Zheng et al. 2013, Jiang et al. 2013, 2014, 2015a, b). In particular, the ARTIST system developed by the University of Lowell, Center for Atmospheric Research, has been widely used and tested (Gilbert and Smith 1988, Conkright and McNamara 1997, Jacobs et al. 2004, Reinisch et al. 2005, McNamara 2006, Bamford et al. 2008, Stankov et al. 2012). Although much progress has been made, there are many issues that have still to be faced, and a significant work is being continuously made to upgrade existing programs. The aim of these improvements is, on the one hand, to advance the reliability of the automatically scaled data, and on the other hand to adapt some systems for being installed in ionosondes that are not equipped with a tool to automatically scale the recorded trace.

One type of ionosonde that is built without being equipped with an automatic scaling system is the Canadian Advanced Digital Ionosonde (CADI) (MacDougall et al. 1993). The present paper considers a dataset of ionograms recorded by the CADI ionosonde installed at São José dos Campos (SJC) (23.2°S, 45.9°W, magnetic latitude 14.1°S), Brazil, and discusses the results obtained after applying two different autoscaling systems, Autoscala, developed at Istituto Nazionale di Geofisica e Vulcanologia, Rome, Italy (Pezzopane and Scotto 2005, 2007, 2010), and the UNIVAP Digital Ionosonde Data Analysis-scaling (UDIDA-scaling, hereafter UDIDA), developed at the Laboratório de Física e Astronomia of the Universidade do Vale do Paraíba (UNIVAP), São José dos Campos, Brazil (Pillat et al. 2013).

The main characteristic of Autoscala is that it is based on an image recognition technique, which makes the algorithm unrelated to the hardware features of the ionosonde, and consequently able to scale ionograms independently of the information on the polarization tagging. The algorithm gives as output the main characteristics of the F2, F1, E, and Es ionospheric layers, as well as an estimation of the vertical electron density profile (Scotto 2009), and it has been applied to different types of ionosonde (Pezzopane and Scotto 2004, Scotto and Pezzopane 2008, Bullett et al. 2010, Krasheninnikov et al. 2010, Pezzopane et al. 2010, Scotto and MacDougall 2012, Enell et al. 2016).

UDIDA uses a fuzzy relation to fit the trace and gives as output the following F region characteristics: the critical frequency of the F region (foF2), the virtual height of the base of the F region (h’F), and the F region peak height (hpF2 = h(foF2·0.834)) (Piggott and Rawer 1972).

In this paper, ionograms recorded at SJC for quiet and disturbed periods are autoscaled by both Autoscala and UDIDA. The dataset considered, how the data analysis has been carried out, and the corresponding results are described in Section 2. The discussion and conclusions are the subject of Sections 3 and 4, respectively.

DATASETS,  ANALYSES  AND  RESULTS

The ionograms considered to compare the two autoscaling systems, Autoscala and UDIDA, are divided in two groups. The first group includes the hourly ionograms recorded at SJC for high solar activity (R12 = 116) in September 2000, for medium solar activity (R12 = 47) in March 2004, and for low solar activity (R12 = 2) in November 2008, and it represents the “quiet” dataset, even though a geomagnetic storm occurred on 17-20 September 2000 (Dst = -201 nT). The second group, which represents the “disturbed” dataset, includes the 5-minute ionograms recorded at SJC during three different geomagnetic storms occurred on 24-26 August 2005 (Dst  = -184 nT), on 14-16 December 2006 (Dst  = -162 nT), and on 24-26 October 2011 (Dst  = -147 nT), and during the well-known and well-studied St. Patrick storm occurred on 17-19 March 2015 (Dst  = -223 nT) (Astafyeva et al. 2015, Carter et al. 2016, De Michelis et al. 2016, Nava et al. 2016, Nayak et al. 2016, Pignalberi et al. 2016, Spogli et al. 2016, Tulasi et al. 2016, Zhong et al. 2016).

It is worth highlighting that to process CADI ionograms with Autoscala it was necessary to perform an ionogram file format conversion from the MD4 one, which is the native CADI format, to the RDF format (Pezzopane 2004), which is the format with which the Autoscala system was run since the early stage of its development. This format conversion did not cause any loss of information, as it is shown in Figs. 1a, b for typical nighttime and daytime ionograms.

Fig. 1a. Examples of conversion from (top) the MD4 format to (bottom) the RDF format for the ionogram recorded at SJC on 1 September 2000 at 06:00 UT.

Fig. 1b. Same as Fig. 1a but for the ionogram recorded at SJC on 13 November 2008 at 13:00 UT.

In order to evaluate the two autoscaling systems, automatically scaled values of foF2 are compared with the ones hand-scaled by an experienced operator. We chose to carry out the test by considering the ionospheric characteristic foF2 because for this one both systems obtained the most reliable results. Moreover, with reference to the processing dataset of ionograms, the following subsets were considered: subset 1, including ionograms for which both the autoscaling system and the operator give a value as output; subset 2, including ionograms for which neither the autoscaling system nor the operator give a value as output; subset 3, including ionograms for which the autoscaling system gives a value as output, while the operator does not; subset 4, including ionograms for which the operator gives a value as output, while the autoscaling system does not.

Tables 1-7 show the results obtained after applying both Autoscala and UDIDA on each of the seven single periods (the three quiet months and the four disturbed periods) forming the whole considered dataset of ionograms recorded at SJC. For each table the top part (named as “Autoscaling statistics”) shows the number of ionograms falling in each subset (1, 2, 3 or 4), while the bottom part (named as “Autoscaling accuracy subset 1”) shows the autoscaling accuracy related to subset 1, in terms of 4 different ranges (xa ≤ 0.5, 0.5 < xa ≤ 1.0, 1.0 < xa ≤ 1.5, and xa > 1.5) of the absolute error xa = |autoscaled value – validated value|, and in terms of 4 different ranges (xr ≤ 0.1, 0.1 < xr ≤ 0.3, 0.3 < xr ≤ 0.5, and xr > 0.5) of the relative error xr = (|autoscaled value – validated value|/validated value). In both cases, a distinction between daytime ionograms (recorded between 6:00 and 18:00 LT) and nighttime ionograms (recorded between 18:00 and 6:00 LT) was also made.

Table 1

The autoscaling statistics (see the text for the description of the four different subsets), and the corresponding autoscaling accuracy for subset 1, are shown for both Autoscala and UDIDA for the hourly ionograms recorded in September 2000 (R12 = 116). Concerning the “Autoscaling statistics”: the percentages between brackets of Autoscala for subset 1 and subset 4 refer to the total number of ionograms of (subset 1 + subset 4), that is, the ionograms for which the operator gave a value of foF2 as output; the percentages between brackets of Autoscala for subset 2 and subset 3 refer to the total number of ionograms of (subset 2 + subset 3), that is, the ionograms for which the operator did not give any value of foF2 as output.

| September 2000 (R12 = 116) (603 ionograms) |
| --- |
| Autoscaling statistics |
|  | Autoscala | UDIDA |
| subset 1 | 137 (~37%) | 369 |
| subset 2 | 229 (~98%) | - |
| subset 3 | 5 (~2%) | 234 |
| subset 4 | 232 (~63%) | - |
| Autoscaling accuracy subset 1 |
| xa = ¦autoscaled value – validated value¦ [MHz] | Autoscala (137 ionograms) | UDIDA (369 ionograms) |
|  | Total ionograms (137) | Daytime ionograms (59) | Nighttime ionograms (78) | Total ionograms (369) | Daytime ionograms (242) | Nighttime ionograms (127) |
| xa ≤ 0.5 | 127 (~93%) | 53 (~90%) | 74 (~95%) | 265 (~72%) | 165 (~68%) | 100 (~79%) |
| 0.5 < xa ≤ 1.0 | 5 (~3%) | 2 (~3%) | 3 (~4%) | 52 (~14%) | 37 (~15%) | 15 (~12%) |
| 1.0 < xa ≤ 1.5 | - | - | - | 35 (~10%) | 28 (~12%) | 7 (~5%) |
| xa > 1.5 | 5 (~3%) | 4 (~7%) | 1 (~3%) | 17 (~4%) | 12 (~5%) | 5 (~4%) |
| xr = ¦autoscaled value – validated value¦/ validated value | Autoscala (137 ionograms) | UDIDA (369 ionograms) |
|  | Total ionograms (137) | Daytime ionograms (59) | Nighttime ionograms (78) | Total ionograms (369) | Daytime ionograms (242) | Nighttime ionograms (127) |
| xr ≤ 0.1 | 130 (~95%) | 55 (~93%) | 75 (~96%) | 328 (~89%) | 221 (~91%) | 107 (~84%) |
| 0.1 < xr ≤ 0.3 | 3 (~2%) | 1 (~2%) | 2 (~3%) | 35 (~9%) | 17 (~7%) | 18 (~14%) |
| 0.3 < xr ≤ 0.5 | 3 (~2%) | 2 (~3%) | 1 (~1%) | 3 (~1%) | 1 (~1%) | 2 (~2%) |
| xr > 0.5 | 1 (~1%) | 1 (~2%) | - | 3 (~1%) | 3 (~1%) | - |

Table 2

Same as Table 1 but for March 2004 (R12 = 47)

| March 2004 (R12 = 47) (627 ionograms) |
| --- |
| Autoscaling statistics |
|  | Autoscala | UDIDA |
| subset 1 | 265 (~51%) | 522 |
| subset 2 | 85 (~81%) | - |
| subset 3 | 20 (~19%) | 105 |
| subset 4 | 257 (~49%) | - |
| Autoscaling accuracy subset 1 |
| xa = ¦autoscaled value – validated value¦ [MHz] | Autoscala (265 ionograms) | UDIDA (522 ionograms) |
|  | Total ionograms (265) | Daytime ionograms (125) | Nighttime ionograms (140) | Total ionograms (522) | Daytime ionograms (316) | Nighttime ionograms (206) |
| xa ≤ 0.5 | 241 (~91%) | 110 (~88%) | 131 (~94%) | 278 (~53%) | 183 (~58%) | 95 (~46%) |
| 0.5 < xa ≤ 1.0 | 20 (~7%) | 11 (~8%) | 9 (~6%) | 109 (~21%) | 62 (~20%) | 47 (~22%) |
| 1.0 < xa ≤ 1.5 | 2 (~1%) | 2 (~2%) | - | 87 (~17) | 55 (~17%) | 32 (~16%) |
| xa > 1.5 | 2 (~1%) | 2 (~2%) | - | 48 (~8%) | 16 (~5%) | 32 (~16%) |
| xr = ¦autoscaled value – validated value¦/ validated value | Autoscala (265 ionograms) | UDIDA (522 ionograms) |
|  | Total ionograms (265) | Daytime ionograms (125) | Nighttime ionograms (140) | Total ionograms (522) | Daytime ionograms (316) | Nighttime ionograms (206) |
| xr ≤ 0.1 | 247 (~93%) | 117 (~94%) | 130 (~93%) | 379 (~73%) | 261 (~83%) | 118 (~57%) |
| 0.1 < xr ≤ 0.3 | 18 (~7%) | 8 (~6%) | 10 (~7%) | 94 (~18%) | 43 (~13%) | 51 (~25%) |
| 0.3 < xr ≤ 0.5 | - | - | - | 30 (~6%) | 8 (~3%) | 22 (~11%) |
| xr > 0.5 | - | - | - | 19 (~3%) | 4 (~1%) | 15 (~7%) |

Table 3

Same as Table 1 but for November 2008 (R12 = 2)

| November 2008 (R12 = 2) (510 ionograms) |
| --- |
| Autoscaling statistics |
|  | Autoscala | UDIDA |
| subset 1 | 228 (~53%) | 428 |
| subset 2 | 61 (~74%) | - |
| subset 3 | 21 (~26%) | 82 |
| subset 4 | 200 (~47%) | - |
| Autoscaling accuracy subset 1 |
| xa = ¦autoscaled value – validated value¦ [MHz] | Autoscala (228 ionograms) | UDIDA (428 ionograms) |
|  | Total ionograms (228) | Daytime ionograms (93) | Nighttime ionograms (135) | Total ionograms (428) | Daytime ionograms (234) | Nighttime ionograms (194) |
| xa ≤ 0.5 | 224 (~98%) | 93 (100%) | 131 (~97%) | 270 (~63%) | 153(~65%) | 117 (~60%) |
| 0.5 < xa ≤ 1.0 | 4 (~2%) | - | 4 (~3%) | 47 (~11%) | 18 (~8%) | 29 (~15%) |
| 1.0< xa ≤1.5 | - | - | - | 31 (~7%) | 14 (~6%) | 17 (~9%) |
| xa > 1.5 | - | - | - | 80 (~19%) | 49 (~21%) | 31 (~16%) |
| xr = ¦autoscaled value – validated value¦/ validated value | Autoscala (228 ionograms) | UDIDA (428 ionograms) |
|  | Total ionograms (228) | Daytime ionograms (93) | Nighttime ionograms (135) | Total ionograms (428) | Daytime ionograms (234) | Nighttime ionograms (194) |
| xr ≤ 0.1 | 219 (~96%) | 92 (~99%) | 127 (~94%) | 282 (~66%) | 168 (~72%) | 114 (~59%) |
| 0.1 < xr ≤ 0.3 | 9 (~4%) | 1 (~1%) | 8 (~6%) | 73 (~17%) | 28 (~12%) | 45 (~23%) |
| 0.3 < xr ≤ 0.5 | - | - | - | 26 (~6%) | 14 (~6%) | 12 (~6%) |
| xr > 0.5 | - | - | - | 47 (~11%) | 24 (~10%) | 23 (~12%) |

Table 4

Same as Table 1 but for the 5-minutes ionograms recorded on 24-26 August 2005, 
a disturbed period characterized by a Dst of -184 nT

| Storm 24-26 August 2005 (Dst = -184 nT) (826 ionograms) |
| --- |
| Autoscaling statistics |
|  | Autoscala | UDIDA |
| subset 1 | 507 (~80%) | 635 |
| subset 2 | 122 (~64%) | - |
| subset 3 | 69 (~36%) | 191 |
| subset 4 | 128 (~20%) | - |
| Autoscaling accuracy subset 1 |
| xa = ¦autoscaled value – validated value¦ [MHz] | Autoscala (507 ionograms) | UDIDA (635 ionograms) |
|  | Total ionograms (507) | Daytime ionograms (254) | Nighttime ionograms (253) | Total ionograms (635) | Daytime ionograms (362) | Nighttime ionograms (273) |
| xa ≤ 0.5 | 493 (~97%) | 248 (~97%) | 245 (~97%) | 325 (~51%) | 212 (~59%) | 113 (~41%) |
| 0.5 < xa ≤ 1.0 | 11 (~2%) | 4 (~2%) | 7(~2%) | 124 (~20%) | 62 (~17%) | 62 (~23%) |
| 1.0 < xa ≤ 1.5 | 1 (~0.5%) | - | 1 (~1%) | 78 (~12%) | 19 (~5%) | 59 (~22%) |
| xa > 1.5 | 2 (~0.5%) | 2 (~1%) | - | 108 (~17%) | 69 (~19%) | 39 (~14%) |
| xr = ¦autoscaled value – validated value¦/validated value | Autoscala (507 ionograms) | UDIDA (635 ionograms) |
|  | Total ionograms (507) | Daytime ionograms (254) | Nighttime ionograms (253) | Total ionograms (635) | Daytime ionograms (362) | Nighttime ionograms (273) |
| xr ≤ 0.1 | 488 (~96%) | 249 (~98%) | 239 (~94%) | 338 (~53%) | 239 (~66%) | 99 (~36%) |
| 0.1 < xr ≤ 0.3 | 19 (~4%) | 5 (~2%) | 14 (~6%) | 150 (~24%) | 63 (~17%) | 87 (~32%) |
| 0.3 < xr ≤ 0.5 | - | - | - | 72 (~11%) | 24 (~7%) | 48 (~18%) |
| xr > 0.5 | - | - | - | 75 (~12%) | 36 (~10%) | 39 (~14%) |

Table 5

Same as Table 1 but for the 5-minutes ionograms recorded on 
14-16 December 2006, a disturbed period characterized by a Dst of -162 nT

| Storm 14-16 December 2006 (Dst = -162 nT) (860 ionograms) |
| --- |
| Autoscaling statistics |
|  | Autoscala | UDIDA |
| subset 1 | 316 (~48%) | 658 |
| subset 2 | 133 (~66%) | - |
| subset 3 | 69 (~34%) | 202 |
| subset 4 | 342 (~52%) | - |
| Autoscaling accuracy subset 1 |
| xa = ¦autoscaled value – validated value¦ [MHz] | Autoscala (316 ionograms) | UDIDA (658 ionograms) |
|  | Total ionograms (316) | Daytime ionograms (157) | Nighttime ionograms (159) | Total ionograms (658) | Daytime ionograms 423) | Nighttime ionograms (235) |
| xa ≤ 0.5 | 292 (~92%) | 140 (~89%) | 152 (~96%) | 300 (~46%) | 195 (~46%) | 105 (~45%) |
| 0.5 < xa ≤ 1.0 | 22 (~7%) | 15 (~9%) | 7 (~4%) | 101 (~15%) | 62 (~15%) | 39 (~17%) |
| 1.0 < xa ≤1.5 | 1 (~0.5%) | 1 (~1%) | - | 73 (~11%) | 46 (~11%) | 27 (~11%) |
| xa > 1.5 | 1 (~0.5%) | 1 (~1%) | - | 184 (~28%) | 120 (~28%) | 64 (~27%) |
| xr = ¦autoscaled value – validated value¦/ validated value | Autoscala (316 ionograms) | UDIDA (658 ionograms) |
|  | Total ionograms (316) | Daytime ionograms (157) | Nighttime ionograms (159) | Total ionograms (658) | Daytime ionograms (423) | Nighttime ionograms (235) |
| xr ≤ 0.1 | 296 (~93%) | 144 (~92%) | 152 (~96%) | 367 (~56%) | 256 (~61%) | 111 (~47%) |
| 0.1 < xr ≤ 0.3 | 19 (~6%) | 12 (~7%) | 7 (~4%) | 168 (~25%) | 106 (~25%) | 62 (~27%) |
| 0.3 < xr ≤ 0.5 | 1 (~1%) | 1 (~1%) | - | 56 (~9%) | 27 (~6%) | 29 (~12%) |
| xr > 0.5 | - | - | - | 67 (~10%) | 34 (~8%) | 33 (~14%) |

Table 6

Same as Table 1 but for the 5-minutes ionograms recorded on 24-26 October 2011, 
a disturbed period characterized by a Dst of -147 nT

| Storm 24-26 October 2011 (Dst = -147 nT) (761 ionograms) |
| --- |
| Autoscaling statistics |
|  | Autoscala | UDIDA |
| subset 1 | 103 (~19%) | 539 |
| subset 2 | 203 (~91%) | - |
| subset 3 | 19 (~9%) | 222 |
| subset 4 | 436 (~81%) | - |
| Autoscaling accuracy subset 1 |
| xa = ¦autoscaled value – validated value¦ [MHz] | Autoscala (103 ionograms) | UDIDA (539 ionograms) |
|  | Total ionograms (103) | Daytime ionograms (55) | Nighttime ionograms (48) | Total ionograms (539) | Daytime ionograms (391) | Nighttime ionograms (148) |
| xa ≤ 0.5 | 84 (~82%) | 37 (~67%) | 47 (~98%) | 253 (~47%) | 192 (~49%) | 61 (~41%) |
| 0.5 < xa ≤ 1.0 | 10 (~10%) | 9 (~16%) | 1 (~2%) | 137 (~25%) | 92 (~24%) | 45 (~30%) |
| 1.0 < xa ≤ 1.5 | 2 (~1%) | 2 (~4) | - | 100 (~19%) | 71 (~18%) | 29 (~20%) |
| xa > 1.5 | 7 (~7%) | 7 (~13%) | - | 49 (~9%) | 36 (~9%) | 13 (~9%) |
| xr = ¦autoscaled value – validated value¦/validated value | Autoscala (103 ionograms) | UDIDA (539 ionograms) |
|  | Total ionograms (103) | Daytime ionograms (55) | Nighttime ionograms (48) | Total ionograms (539) | Daytime ionograms (391) | Nighttime ionograms (148) |
| xr ≤ 0.1 | 92 (~89%) | 44 (~80%) | 48 (100%) | 424 (~79%) | 314 (~80%) | 110 (~74%) |
| 0.1 < xr ≤ 0.3 | 9 (~9%) | 9 (~16%) | - | 102 (~18%) | 70 (~18%) | 32 (~22%) |
| 0.3 < xr ≤ 0.5 | 1 (~1%) | 1 (~2%) | - | 9 (~2%) | 4 (~1%) | 5 (~3%) |
| xr > 0.5 | 1 (~1%) | 1 (~2%) | - | 4 (~1%) | 3 (~1%) | 1 (~1%) |

Table 7

Same as Table 1 but for the 5-minutes ionograms recorded on 17-19 March 2015, 
a disturbed period characterized by a Dst of -223 nT

| St. Patrick storm 17-19 March 2015 (Dst = -223 nT) (864 ionograms) |
| --- |
| Autoscaling statistics |
|  | Autoscala | UDIDA |
| subset 1 | 269 (~46%) | 613 |
| subset 2 | 216 (~86%) | - |
| subset 3 | 35 (~14%) | 251 |
| subset 4 | 344 (~57%) | - |
| Autoscaling accuracy subset 1 |
| x = ¦autoscaled value – validated value¦ [MHz] | Autoscala (269 ionograms) | UDIDA (613 ionograms) |
|  | Total ionograms (269) | Daytime ionograms (135) | Nighttime ionograms (134) | Total ionograms (613) | Daytime ionograms (352) | Nighttime ionograms (261) |
| x ≤ 0.5 | 250 (~93%) | 125 (~93%) | 125 (~93%) | 238 (~39%) | 143 (~41%) | 95 (~36%) |
| 0.5 < x ≤ 1.0 | 16 (~6%) | 7 (~5%) | 9 (~7%) | 110 (~18%) | 59 (~17%) | 51 (~20%) |
| 1.0 < x ≤ 1.5 | 3 (~1%) | 3 (~2%) | - | 97 (~16%) | 68 (~19%) | 29 (~11%) |
| x > 1.5 | - | - | - | 168 (~27%) | 82 (~23%) | 86 (~33%) |
| x = ¦autoscaled value – validated value¦/ validated value | Autoscala (269 ionograms) | UDIDA (613 ionograms) |
|  | Total ionograms (269) | Daytime ionograms (135) | Nighttime ionograms (134) | Total ionograms (613) | Daytime ionograms (352) | Nighttime ionograms (261) |
| x ≤ 0.1 | 252 (~94%) | 129 (~96%) | 123 (~92%) | 357 (~58%) | 229 (~65%) | 128 (~49%) |
| 0.1 < x ≤ 0.3 | 17 (~6%) | 6 (~4%) | 11 (~8%) | 146 (~24%) | 84 (~24%) | 62 (~24%) |
| 0.3 < x ≤ 0.5 | - | - | - | 50 (~8%) | 24 (~7%) | 26 (~10%) |
| x > 0.5 | - | - | - | 60 (~10%) | 15 (~4%) | 45 (~17%) |

Moreover, for each of the seven considered periods, corresponding linear fits between autoscaled and validated values of subset 1 are shown for Autoscala and UDIDA in Figs. 2 and 3, for quiet and disturbed periods, respectively; the number visible at the bottom right corner of each plot is the Pearson correlation coefficient, according to the following formula

,  	(1)

where cov() is the covariance between the variables X and Y, σX and σY are the corresponding standard deviations, and E() represents the expected value. Specifically, in order to compare the performances of both autoscaling systems at the same level, besides showing the linear fits for the whole subset 1 of Autoscala (left columns of plots) and for the whole subset 1 of UDIDA (right column of plots), Figs. 2 and 3 show also the linear fits for the part of subset 1 of UDIDA, which is coincident with the subset 1 of Autoscala (middle column of plots).

Fig. 2. Linear fits (in red the regression line, the slope and the intercept values of which are reported at the bottom of each plot) for the whole subset 1 (see the text for the description of the four different subsets) of Autoscala (left column), for the whole subset 1 of UDIDA (right column), and for the part of subset 1 of UDIDA, which is coincident with the subset 1 of Autoscala (middle column), for the quiet periods of September 2000, March 2004, and November 2008. The value of the Pearson correlation coefficient is reported at the bottom right corner of each plot.

Fig. 3. Same as Fig. 2 but for the disturbed periods occurred on 24-26 August 2005, 14-16 December 2006, 24-26 October 2011, and 17-19 March 2015.

DISCUSSION

Looking at Tables 1-7, the different philosophy characterizing the two autoscaling systems is evident. On the one hand, UDIDA gives always a value for foF2, independently of the presence of the ionogram trace and, if present, independently of its definition; on the other hand, Autoscala tends to discard ionograms for which the digital information is considered insufficient, giving no value of foF2 as output. This different kind of processing explains why the number of ionograms falling in the subset 1 is greater for UDIDA than for Autoscala, while the number of ionograms falling in the subset 4 is greater for Autoscala than for UDIDA. In fact, for both quiet and disturbed conditions, and independently of the solar activity, the trace referring to the F2 layer is weak and scarcely defined for most of the ionograms, and consequently Autoscala does not give any foF2 value as output. As an example, Fig. 4 shows an ionogram for which the operator scaled a value of 11.0 MHz for foF2, while Autoscala considered the digital information insufficient to identify the ionogram trace. This Autoscala behavior might be smoothed by varying the thresholds used by the algorithm to identify the F2 trace, but this is a long and hard task that could be done as a further step.

At the same time, however, this feature allows Autoscala to identify correctly the ionogram cases for which the operator did not validate any foF2 value, and in fact the number of ionograms falling in the subset 2 for Autoscala is high. On the contrary, UDIDA cannot identify this kind of ionograms, and correspondingly the number of ionograms falling in the subset 3 is large. This is a feature of UDIDA that has to be certainly improved in the near future; namely, this system should be equipped with a subroutine able to reliably identify whether the ionogram trace is absent or not.

Fig. 4. Example of ionogram for which the operator scales a value of 11.0 MHz for foF2, while Autoscala does not give any value as output.

Figures 5 and 6 show two examples of ionograms falling in the subsets 1 and 3, respectively, as processed by Autoscala and UDIDA.

Fig. 5. Example of ionogram of subset 1 as autoscaled by (top) UDIDA and (bottom) Autoscala. The red curve in the top panel is the ionogram reconstructed by UDIDA, while the blue and the green curve in the bottom panel are, respectively, the ionogram reconstructed and the corresponding vertical electron density profile given by Autoscala.

Concerning the number of ionograms falling in subset 3, this shows a tendency to increase for both Autoscala and UDIDA for disturbed periods. For Autoscala, also the number of ionograms falling in the subset 4 seems to increase for disturbed periods.

Concerning the number of ionograms falling in the subset 1, for both UDIDA and Autoscala it seems to be independent of both the period and the solar activity.

Focusing the attention on the accuracy of the autoscaling of ionograms of subset 1, this is very high for Autoscala, regardless of both the considered period and the solar activity, while for UDIDA it decreases for disturbed periods. Moreover, Tables 1-7 show also that the accuracy of the UDIDA autoscaling seems to slightly decrease for nighttime ionograms. As it is shown in Fig. 7, this is mainly due to the occurrence of multiple reflections of the sporadic E (Es) layer, and to the presence of noise, which mislead the algorithm, causing as a consequence large absolute and relative errors.

Fig. 6. Same as Fig. 5 but for an ionogram of subset 3.

Fig. 7. Example of nighttime ionograms for which UDIDA was misled by: (a) the presence of noise characterizing the ionogram trace, and (b) the appearance of multiple reflections of the Es layer.

The high accuracy characterizing the autoscaling made by Autoscala can be also inferred by looking at Figs. 2-3, where the linear fits related to Autoscala are all very good, with values of the Pearson correlation coefficient ranging from 0.87 to 0.99. This means that when Autoscala gives a value of foF2 as output, this is very reliable.

Instead, the linear fits related to UDIDA, except the cases of September 2000 and March 2004, are worse than those related to Autoscala, showing a more significant spread of the points, with values of the Pearson correlation coefficient that are lower, especially for disturbed periods.

The main causes of error for UDIDA are then: (1) the presence of spread-F (Fig. 6); (2) the presence of noise (Fig. 7a); (3) the appearance of multiple reflections of the sporadic E layer (Fig. 7b); (4) the appearance of multiple reflections of the F layer (Fig. 8). Concerning (1), UDIDA considers the trace definite enough even though it is characterized by a strong spread-F phenomenon which induces unreliable foF2 values; concerning (2), the presence of clusters of points due to noise causes a wrong identification of the trace and a consequent overestimation of the value given as output; concerning (3) and (4), UDIDA is misled by traces that are not those of the real ionogram. A significant effort has been invested by the UDIDA research team to smooth such errors (Pillat et al. 2015).

Fig. 8. Example of ionogram for which UDIDA was misled by the appearance on the ionograms of multiple reflections of the F layer.

Autoscala instead can manage quite well the presence of multiple reflections (Scotto and Pezzopane 2008), and the main causes of error are: (1) a pronounced weakness of the trace (Fig. 4); (2) the presence of spread F (Fig. 6); (3) the appearance of additional stratifications of the F layer (Lynn et al. 2000, Fagundes et al. 2007) (Fig. 9). Concerning (1), as it was previously mentioned, this malfunctioning of Autoscala might be mitigated by working on thresholds used by the algorithm; concerning (2), it is worth highlighting that most of the ionograms characterized by spread-F phenomena are correctly identified by Autoscala as not identifiable; concerning (3), the problem is known (Scotto 2009) and more complex to be fixed, because it implies a reconsideration of the empirical curves used by Autoscala to identify the different parts of the ionogram; at the same time, Fig. 9 shows that UDIDA can manage better than Autoscala the presence of additional stratifications of the F layer.

Fig. 9. Example of ionogram characterized by the appearance of additional stratifications of the F layer for which (top) UDIDA gives as output a reliable value of foF2, while (bottom) Autoscala performs a strong underestimation of it.

CONCLUSIONS

By considering ionograms recorded by the CADI ionosonde installed at SJC, for quiet and disturbed periods, two autoscaling systems, Autoscala and UDIDA, were compared. UDIDA gives a value of foF2 for each analyzed ionogram, while Autoscala tends to reject ionograms for which the digital information is considered insufficient, and no value of foF2 is given as output. This means that UDIDA can give more foF2 values as output than Autoscala, and that Autoscala can correctly discard a large number of ionograms for which the operator does not validate any foF2 value. With regard to the dependence of the autoscaling on the period and the solar activity, when the operator validates a value of foF2, the capacity of both autoscaling systems in giving a value as output does not present any kind of pattern. Instead, the rejection made by Autoscala for ionograms validated by an operator seems to increase for disturbed conditions. The same pattern seems to characterize the number of ionograms not validated by an operator and incorrectly autoscaled by both systems. The accuracy of the autoscaling is very high for Autoscala, independently of both the considered period and solar activity, while UDIDA shows an accuracy decrease both for disturbed periods, mainly because of the presence of multiple reflections of the sporadic E layer, multiple reflections of the F layer, and spread-F, and for nighttime ionograms because of noise. The main shortcomings showed by Autoscala are instead related to the inability in identifying the ionogram when this is characterized by a pronounced weakness of the trace, the presence of spread F, and the appearance of additional stratifications of the F layer.

In order to smooth the aforementioned autoscaling errors made by both systems, so that they can produce more reliable foF2 values, further fine-tuning analysis is needed. This can lead to the development of a reliable real-time monitoring system of the foF2 ionospheric characteristic at SJC.

References

Astafyeva, E., I. Zakharenkova, and M. Förster (2015), Ionospheric response to the 2015 St. Patrick’s Day storm: A global multi-instrumental overview, J. Geophys. Res. 120, 10, 9023-9037, DOI: 10.1002/ 2015JA02629.

Bamford, R.A., R. Stamper, and L.R. Cander (2008), A comparison between the hourly autoscaled and manually scaled characteristics from the Chilton ionosonde from 1996 to 2004, Radio Sci. 43, 1, RS1001, DOI: 10.1029/ 2005RS003401.

Bullett, T., A. Malagnini, M. Pezzopane, and C. Scotto (2010), Application of Autoscala to ionograms recorded by the VIPIR ionosonde, Adv. Space Res. 45, 9, 1156-1172, DOI: 10.1016/j.asr.2010.01.024.

Carter, B.A., E. Yizengaw, R. Pradipta, J.M. Retterer, K. Groves, C. Valladares, R. Caton, C. Bridgwood, R. Norman, and K. Zhang (2016), Global equatorial plasma bubble occurrence during the 2015 St. Patrick’s Day storm, J. Geophys. Res. 121, 1, 894-905, DOI: 10.1002/2015JA022194.

Chartier, A.T., T. Matsuo, J.L. Anderson, N. Collins, T.J. Hoar, G. Lu, C.N. Mitchell, A.J. Coster, L.J. Paxton, and G.S. Bust (2016), Ionospheric data assimilation and forecasting during storms, J. Geophys. Res. 121, 1, 764-778, DOI: 10.1002/2014JA020799.

Chen, Z., S. Wang, S. Zhang, G. Fang, and J. Wang (2013), Automatic scaling of F layer from ionograms, Radio Sci. 48, 3, 334-343, DOI: 10.1002/rds.20038.

Conkright, R.O., and L.F. McNamara (1997), Quality control of automatically scaled vertical incidence ionogram data, Radio Sci. 32, 5, 1997-2002, DOI: 10.1029/97RS01031.

De Michelis, P., G. Consolini, R. Tozzi, and M.F. Marcucci (2016), Observations of high-latitude geomagnetic field fluctuations during St. Patrick’s Day storm: Swarm and SuperDARN measurements, Earth Planets Space 68, 105, 1-16, DOI: 10.1186/s40623-016-0476-3.

Ding, Z., B. Ning, W. Wan, and L. Liu (2007), Automatic scaling of F2-layer parameters from ionograms based on the empirical orthogonal function (EOF) analysis of ionospheric electron density, Earth Planets Space 59, 1, 51-58, DOI: 10.1186/BF03352022.

Enell, C.-F., A. Kozlovsky, T. Turunen, T. Ulich, S. Välitalo, C. Scotto, and M. Pezzopane (2016), Comparison between manual scaling and Autoscala automatic scaling applied to Sodankylä Geophysical Observatory ionograms, Geosci. Instrum. Method. Data Syst. 5, 53-64, DOI: 10.5194/gi-5-53-2016.

Fagundes, P.R., V. Klausner, Y. Sahai, V.G. Pillat, F. Becker-Guedes, F.C.P. Bertoni, M.J.A. Bolzan, and J.R. Abalde (2007), Observations of daytime F2-layer stratification under the southern crest of the equatorial ionization anomaly region, J. Geophys. Res. 112, A4, A04302, DOI: 10.1029/2006JA011888.

Fox, M.W., and C. Blundell (1989), Automatic scaling of digital ionograms, Radio Sci. 24, 6, 747-761, DOI: 10.1029/RS024i006p00747.

Galkin, I.A., and B.W. Reinisch (2008), The new ARTIST 5 for all digisondes, Ionosonde Netw. Adv. Group Bull. 69, available from: http://www.ips.gov.au/IPSHosted/INAG/web-69/2008/artist5-inag.pdf.

Galkin, I.A., B.W. Reinisch, X. Huang, and D. Bilitza (2012), Assimilation of GIRO data into a real-time IRI, Radio Sci. 47, 4, RS0L07, DOI: 10.1029/ 2011RS004952.

Gardner, L.C., R.W. Schunk, L. Scherliess, J.J. Sojka, and L. Zhu (2014), Global Assimilation of Ionospheric Measurements-Gauss Markov model: Improved specifications with multiple data types, Space Weather 12, 12, 675-688, DOI: 10.1002/2014SW001104.

Gilbert, J.D., and R.W. Smith (1988), A comparison between the automatic ionogram scaling system ARTIST and the standard manual method, Radio Sci. 23, 6, 968-974, DOI: 10.1029/RS023i006p00968.

Igi, S., K. Nozaki, M. Nagayama, A. Ohtani, H. Kato, and K. Igarashi (1993), Automatic ionogram processing systems in Japan. In: Proc. Session G6, 24th General Assembly of the International Union of Radio Science (URSI), 25 August – 2 September 1993, Kyoto, Japan.

Jacobs, L., A.W.V. Poole, and L.A. McKinnel (2004), An analysis of automatically scaled F1 layer data over Grahamstown, South Africa, Adv. Space Res. 34, 9, 1949-1952, DOI: 10.1016/j.asr.2004.06.009.

Jiang, C., G. Yang, Z. Zhao, Y. Zhang, P. Zhu, and H. Sun (2013), An automatic scaling technique for obtaining F2 parameters and F1 critical frequency from vertical incidence ionograms, Radio Sci. 48, 6, 739-751, DOI: 10.1002/2013RS005223.

Jiang, C., G. Yang, Z. Zhao, Y. Zhang, P. Zhu, H. Sun, and C. Zhou (2014), A method for the automatic calculation of electron density profiles from vertical incidence ionograms, J. Atmos. Sol.-Terr. Phys. 107, 20-29, DOI: 10.1016/j.jastp.2013.10.012.

Jiang, C., Y. Zhang, G. Yang, P. Zhu, H. Sun, X. Cui, H. Song, and Z. Zhao (2015a), Automatic scaling of the sporadic E layer and removal of its multiple reflection and backscatter echoes for vertical incidence ionograms, J. Atmos. Sol.-Terr. Phys. 129, 41-48, DOI: 10.1016/j.jastp.2015.04.005.

Jiang, C., G. Yang, T. Lan, P. Zhu, H. Song, C. Zhou, X. Cui, Z. Zhao, and Y. Zhang (2015b), Improvement of automatic scaling of vertical incidence ionograms by simulated annealing, J. Atmos. Sol.-Terr. Phys. 133, 178-184, DOI: 10.1016/j.jastp.2015.09.002.

Krasheninnikov, I., M. Pezzopane, and C. Scotto (2010), Application of Autoscala to ionograms recorded by the AIS-Parus ionosonde, Comp. Geosci. 36, 5, 628-635, DOI: 10.1016/j.cageo.2009.09.013.

Lee, I.T., T. Matsuo, A.D. Richmond, J.Y. Liu, W. Wang, C.H. Lin, J.L. Anderson, and M.Q. Chen (2012), Assimilation of FORMOSAT-3/COSMIC electron density profiles into a coupled thermosphere/ionosphere model using ensemble Kalman filtering, J. Geophys. Res. 117, A10, A10318, DOI: 10.1029/2012JA017700.

Lynn, K.J.W., T.J. Harris, and M. Sjarifudin (2000), Strattification of the F2 layer observed in Southeast Asia, J. Geophys. Res. 105, A12, 27147-27156, DOI: 10.1029/2000JA900056.

MacDougall, J.W., I.F. Grant, and X. Shen (1993), The Canadian Advanced Digital Ionosonde: design and results. In: Proc. 24th General Assembly of the International Union of Radio Science (URSI), 25 August – 2 September 1993, Kyoto, Japan.

McNamara, L.F. (2006), Quality figures and error bars for autoscaled Digisonde vertical incidence ionograms, Radio Sci. 41, 4, RS4011, DOI: 10.1029/ 2005RS003440.

McNamara, L.F., M.J. Angling, S. Elvidge, S.V. Fridman, M.A. Hausman, L.J. Nickisch, and L.A. McKinnell (2013), Assimilation procedures for updating ionospheric profiles below the F2 peak, Radio Sci. 48, 2, 143-157, DOI: 10.1002/rds.20020.

Nava, B., J. Rodríguez‐Zuluaga, K. Alazo‐Cuartas, A. Kashcheyev, Y. Migoya‐ Orué, S.M. Radicella, C. Amory-Mazaudier, and R. Fleury (2016), Middle‐and low‐latitude ionosphere response to 2015 St. Patrick’s Day geomagnetic storm, J. Geophys. Res. 121, 4, 3421-3438, DOI: 10.1002/ 2015JA022299.

Nayak, C., L.-C. Tsai, S.-Y. Su, I.A. Galkin, A.T.K. Tan, E. Nofri, and P. Jamjareegulgarn (2016), Peculiar features of the low-latitude and midlatitude ionospheric response to the St. Patrick’s Day geomagnetic storm of 17 March 2015, J. Geophys. Res. 121, 8, 7941-7960, DOI: 10.1002/ 2016JA022489.

Pezzopane, M. (2004), Interpre: a Windows software for semiautomatic scaling of ionospheric parameters from ionograms, Comp. Geosci. 30, 1, 125-130, DOI: 10.1016/j.cageo.2003.09.009.

Pezzopane, M., and C. Scotto (2004), Software for the automatic scaling of critical frequency foF2 and MUF(3000)F2 from ionograms applied at the Ionospheric Observatory of Gibilmanna, Ann. Geophys. 47, 6, 1783-1790.

Pezzopane, M., and C. Scotto (2005), The INGV software for the automatic scaling of foF2 and MUF(3000)F2 from ionograms: A performance comparison with ARTIST 4.01 from Rome data, J. Atmos. Sol.-Terr. Phys. 67, 12, 1063-1073, DOI: 10.1016/j.jastp.2005.02.022.

Pezzopane, M., and C. Scotto (2007), Automatic scaling of critical frequency foF2 and MUF(3000)F2: A comparison between Autoscala and ARTIST 4.5 on Rome data, Radio Sci. 42, 4, RS4003, DOI: 10.1029/2006RS003581.

Pezzopane, M., and C. Scotto (2010), Highlighting the F2 trace on an ionogram to improve Autoscala performance, Comp. Geosci. 36, 9, 1168-1177, DOI: 10.1016/j.cageo.2010.01.010.

Pezzopane, M., C. Scotto, Ł. Tomasik, and I. Krasheninnikov (2010), Autoscala: an aid for different ionosondes, Acta Geophys. 58, 3, 513-526, DOI: 10.2478/s11600-009-0038-1.

Pezzopane, M., M. Pietrella, A. Pignatelli, B. Zolesi, and L.R. Cander (2011), Assimilation of autoscaled data and regional and local ionospheric models as input sources for real-time 3-D International Reference Ionosphere modeling, Radio Sci. 46, 5, RS5009, DOI: 10.1029/2011RS004697.

Pezzopane, M., M. Pietrella, A. Pignatelli, B. Zolesi, and Lj. R. Cander (2013), Testing the three-dimensional IRI-SIRMUP-P mapping of the ionosphere for disturbed periods, Adv. Space Res. 52, 10, 1726-1736, DOI: 10.1016/ j.asr.2012.11.028.

Piggott, W.R., and K. Rawer (1972), U.R.S.I. Handbook of Ionogram Interpretation and Reduction, World Data Center A for Solar-Terrestrial Physics, NOAA, Boulder, USA.

Pignalberi, A., M. Pezzopane, R. Tozzi, P. De Michelis, and I. Coco (2016), Comparison between IRI and preliminary Swarm Langmuir probe measurements during the St. Patrick storm period, Earth Planets Space 68, 93, 1-18, DOI: 10.1186/s40623-016-0466-5.

Pillat, V.G., L.N.F. Guimaraes, P.R. Fagundes, and J.D.S. da Silva (2013), A computational tool for ionosonde CADI’s ionogram analysis, Comp. Geosci. 52, 372-378, DOI: 10.1016/j.cageo.2012.11.009.

Pillat, V.G., P.R. Fagundes, and L.N.F. Guimaraes (2015), Automatically identification of Equatorial Spread-F occurrence on ionograms, J. Atmos. Sol.-Terr. Phys. 135, 118-125, DOI: 10.1016/j.jastp.2015.10.015.

Reinisch, B.W., and X. Huang (1983), Automatic calculation of electron density profiles from digital ionograms: 3. Processing of bottomside ionograms, Radio Sci. 18, 3, 477-492, DOI: 10.1029/RS018i003p00477.

Reinisch, B.W., X. Huang, I.A. Galkin, V. Paznukhov, and A. Kozlov (2005), Recent advances in real-time analysis of ionograms and ionospheric drift measurements with digisondes, J. Atmos. Sol.-Terr. Phys. 67, 12, 1054-1062, DOI: 10.1016/j.jastp.2005.01.009.

Sabbagh, D., C. Scotto, and V. Sgrigna (2016), A regional adaptive and assimilative three-dimensional ionospheric model, Adv. Space Res. 57, 5, 1241-1257, DOI: 10.1016/j.asr.2015.12.038.

Scotto, C. (2009), Electron density profile calculation technique for Autoscala ionogram analysis, Adv. Space Res. 44, 6, 756-766, DOI: 10.1016/ j.asr.2009.04.037.

Scotto, C., and J. MacDougall (2012), Application of Autoscala software to the Canadian Advanced Digital Ionosonde, Int. J. Remote Sens. 33, 17, 5574-5582, DOI: 10.1080/01431161.2012.661097.

Scotto, C., and M. Pezzopane (2008), Removing multiple reflections from the F2 layer to improve Autoscala performance, J. Atmos. Sol.-Terr. Phys. 70, 15, 1929-1934, DOI: 10.1016/j.jastp.2008.05.012.

Spogli, L., C. Cesaroni, D. Di Mauro, M. Pezzopane, L. Alfonsi, E. Musicò, G. Povero, M. Pini, F. Dovis, R. Romero, N. Linty, P. Abadi, F. Nuraeni, A. Husin, L.H. Minh, T.L. Tran, V.L. The, V.G. Pillat, and N. Floury (2016), Formation of ionospheric irregularities over Southeast Asia during the 2015 St. Patrick’s Day storm, J. Geophys. Res. 121, 12, 12211-12233, DOI: 10.1002/2016JA023222.

Stankov, S.M., J.C. Jodogne, I. Kutiev, K. Stegen, and R. Warnant (2012), Evaluation of automatic ionogram scaling for use in real-time ionospheric density profile specification: Dourbes DGS-256/ARTIST-4 performance, Ann. Geophys. 55, 2, 283-291, DOI: 10.4401/ag-4976.

Su, F., Z. Zhao, S. Li, M. Yao, G. Chen, and Y. Zhou (2012), Signal identification and trace extraction for the vertical ionogram, IEEE Geosci. Remote Sens. Lett. 9, 6, 1031-1035, DOI: 10.1109/LGRS.2012.2189350.

Tsai, L.C., and F.T. Berkey (2000), Ionogram analysis using fuzzy segmentation and connectedness techniques, Radio Sci. 35, 5, 1173-1186, DOI: 10.1029/ 1999RS002170.

Tulasi Ram, S., T. Yokoyama, Y. Otsuka, K. Shiokawa, S. Sripathi, B. Veenadhari, R. Heelis, K.K. Ajith, V.S. Gowtam, S. Gurubaran, P. Supnithi, and M. Le Huy (2016), Duskside enhancement of equatorial zonal electric field response to convection electric fields during the St. Patrick’s Day storm on 17 March 2015, J. Geophys. Res. 121, 1, 538-548, DOI: 10.1002/ 2015JA021932.

Zabotin, N.A., J.W. Wright, and G.A. Zhbankov (2006), NeXtYZ: Three-dimensional electron density inversion for dynasonde ionograms, Radio Sci. 41, 6, RS6S32. DOI: 10.1029/2005RS003352.

Zheng, H., G. Ji, G. Wang, Z. Zhao, and S. He (2013), Automatic scaling of F layer from ionograms based on image processing and analysis, J. Atmos. Sol.-Terr. Phys. 105-106, 110-118, DOI: 10.1016/j.jastp.2013.09.007.

Zhong, J., W. Wang, X. Yue, A.G. Burns, X. Dou, and J. Lei (2016), Long-duration depletion in the topside ionospheric total electron content during the recovery phase of the March 2015 strong storm, J. Geophys. Res. 121, 5, 4733-4747, DOI: 10.1002/2016JA022469.

Received  20 May 2016
Received in revised form  22 December 2016
Accepted  29 December 2016