S11B-0558 0830h POSTER

Improved Seismic Acquisition System and Data Processing for the Italian National Seismic Network

Lucio Badiali1 (39-06-51860352; badiali@ingv.it)

Carlo Marcocci1 (marcocci@ingv.it)

Franco Mele1 (mele@ingv.it)

Alessandro Piscini1 (piscini@ingv.it)

1Istituto Nazionale di Geofisica e Vulcanologia, Via

diVi gna Murata, 605, Rome 00143, Italy

A new system for acquiring and processing digital signals has been developed in the last few years at the Istituto Nazionale di Geofisica e Vulcanologia (INGV). The system makes extensive use of the internet communication protocol standards such as TCP and UDP which are used as the transport highway inside the Italian network, and possibly in a near future outside, to share or redirect data among processes. The Italian National Seismic Network has been working for about 18 years equipped with vertical short period seismometers and transmitting through analog lines, to the computer center in Rome. We are now concentrating our efforts on speeding the migration towards a fully digital network based on about 150 stations equipped with either broad band or 5 seconds sensors connected to the data center partly through wired digital communication and partly through satellite digital communication. The overall process is layered through intranet and/or internet. Every layer gathers data in a simple format and provides data in a processed format, ready to be distributed towards the next layer. The lowest level acquires seismic data (raw waveforms) coming from the remote stations. It handshakes, checks and sends data in LAN or WAN according to a distribution list where other machines with their programs are waiting for. At the next level there are the picking procedures, or pickers, on a per instrument basis, looking for phases. A picker spreads phases, again through the LAN or WAN and according to a distribution list, to one or more waiting locating machines tuned to generate a seismic event. The event locating procedure itself, the higher level in this stack, can exchange information with other similar procedures. Such a layered and distributed structure with nearby targets allows other seismic networks to join the processing and data collection of the same ongoing event, creating a virtual network larger than the original one. At present we plan to cooperate with other Italian regional and local networks, and with the VBB Mediterranean Network (MedNet) to share waveforms and events detected in real time. The seismic acquisition system at INGV uses a relational database built on standard SQL, for every activity involving the seismic network.