Horizontal and vertical ground motion prediction equations derived from the Italian Accelerometric Archive (ITACA)

D. Bindi(1), L. Luzi(1), M. Massa(1), F. Pacor(1)

(1) Istituto Nazionale di Geofisica e Vulcanologia, Via Bassini 15, 20133 Milano, Italy

Corresponding Author: Dino Bindi, bindi@mi.ingv.it, tel +39 0223699270, fax +39 0223699458

Abstract

A set of Ground Motion Prediction Equations (GMPEs) for the Italian territory is proposed, exploiting a new strong-motion data set become available since July 2007. The data set is composed by 561 three-component waveforms from 107 earthquakes with moment magnitude in the range 4 - 6.9, occurred in Italy from 1972 to 2007 and recorded by 206 stations at distances up to100 km. The functional form used to derive GMPEs in Italy (Sabetta and Pugliese, 1996) has been modified introducing a quadratic term for magnitude and a magnitude-dependent geometrical spreading . The coefficients for the prediction of horizontal and vertical peak ground acceleration, peak ground velocity and 5% damped acceleration response spectra are evaluated. This paper illustrates the new data set, the regression analysis and the comparisons with recently derived GMPEs in Europe and in the Next Generation Attenuation of Ground Motions (NGA) Project.

Keywords: ground motion prediction equation, strong ground motion, peak ground acceleration, peak ground velocity, acceleration response spectra

1. Introduction

The prediction of the ground motion as a function of source-to-site distance and earthquake magnitude is required for assessing the seismic hazard of a given site or an area. The probabilistic approach to seismic hazard (Cornell, 1968) determines the ground motion level at a fixed probability of exceedence over a selected time interval, using the ground motion predicted by a Ground Motion Prediction Equation (GMPE) in terms of mean values and related uncertainties. The GMPEs are generally developed by the regression analysis of a set of observations which results in a set of coefficients of an assumed ground motion model. Besides the earthquake magnitude and the source-to-site distance, the explanatory variables of the ground motion model generally include several terms describing the source (e.g. style of faulting, hanging/foot wall effects, etc.) or the site (e.g. soil class, resonant frequency, etc.). The complexity of the model should be suitable to the characteristics of the data set and should return reliable values of the explanatory variables.

The earliest GMPEs in Italy were developed by Sabetta and Pugliese (1987), hereinafter SP87, for evaluating the peak ground acceleration and velocity and subsequently extended to 5% damped pseudo-velocity response spectra (Sabetta and Pugliese, 1996, hereinafter SP96). The authors exploited a data set consisting of 17 earthquakes occurred in the period 1976-1984, with a magnitude range 4.6-6.8 (local or surface wave magnitude) and recorded at distances smaller than 115 km from the causative fault.

Further GMPEs have been recently developed for different regions in Italy, considering different explanatory variables and magnitude -distance ranges. For example, regional GMPEs have been calibrated for North-Eastern Italy (Bragato and Slejko, 2005; Ml ranges 2.5-6.3 for epicentral or fault distances up to 130 km), for North-Western Italy (Frisenda et al., 2005; Ml up to 4.5 and hypocentral distances up to 200 km), Northern-Italy (Massa et al., 2008; Ml range 3.5 – 6.3 and epicentral distances up to 100 km) and Umbria-Marche (Central Italy) region (Bindi et al., 2006; Ml range 4-6 for epicentral and hypocentral distances up to 100 km).

The goodness of fit of the Italian GMPE developed by Sabetta and Pugliese (1987; 1996) has been recently evaluated by considering a subset with the 27 major earthquakes occurred in Italy from 1972 to 2002 (Bindi et al., 2009). The results showed that these GMPEs do not adequately fit the new strong-motion data set, for its small standard deviation and its non-zero bias, especially for rock sites. Moreover, the analysis of the residuals highlighted the inadequacy of the selected functional form to capture the behaviour of the attenuation of the strong motion parameters with distance (Bindi et al., 2009).

In this study, we exploit the new Italian strong motion archive (ITalian ACcelerometric Archive ITACA http://itaca.mi.ingv.it, Luzi et al., 2008) to develop new empirical GMPEs for Italy. The models are developed for peak ground acceleration, peak ground velocity and 5% damped acceleration response spectra, considering both the maximum horizontal and vertical component of motions. The functional form considered by SP96 has been modified introducing a quadratic term for magnitude and a magnitude-dependent geometrical spreading.

2. Data set and Data processing

The GMPEs were developed considering the strong motion records processed in the ITACA archive (Luzi et al., 2008). In particular, the raw accelerometric time series has been filtered using a fourth order a-causal Butterworth filter, selecting the corner frequencies by visual inspection of the Fourier spectrum of individual records. Details about data processing and different choices adopted for digital and analogue records can be found in Massa et al. (2009, this issue).

To develop the new GMPEs, we selected in the database earthquakes with moment magnitude larger than or equal to 4 and distances from the fault smaller than 100 km, recorded at least by two stations. In addition we included the waveforms recorded by the Northern Italy Strong Motion network (Rete Accelerometrica dell’Italia Settentrionale, RAIS http://rais.mi.ingv.it/), installed around the Garda lake area, in northern Italy. They correspond to three events occurred in 2006 and 2007 (id’s from 105 to 107 in Table 1), with magnitudes in the range 4.2 – 4.5. Since a detailed geophysical characterization is available only for a small subset of sites, the stations were grouped according to the site classifications used in SP87, consisting of three classes. The first class (hereinafter referred to as C0) includes the stations installed on rock; the second class (C1) includes the stations installed on shallow sediments (thinner than 20 m) while the third class (C2) is representative of the stations installed on sediments thicker than 20m, where with the term “sediment” are denoted soils with shear wave velocity lower than 800 m/s. Class C0 corresponds to classes A and B of NEHRP site classification, while the classification of soil stations using classes C1 and C2 (which roughly corresponding to classes C and D of NEHRP, respectively) is simple but efficient in identifying the sites with amplifications occurring at frequencies larger or smaller than about 2-5 Hz

The selected data set is composed by 107 earthquakes and 206 stations with the geographical distribution shown in Figure 1. The characteristics of the earthquakes are listed in Table 1, whereas the magnitude versus the horizontal distance to the surface projection of the fault plane (Joyner and Boore distance, Rjb) distribution is shown in Figure 2. ,  The Rjb has been computed for the events with M ≥ 5.5 using the fault geometry reported in the DISS database (DISS Working Group, 2006; Basili et al., 2008) while the epicentral distance is used for earthquakes with smaller magnitude. Magnitudes up to 6 are well sampled at distances greater than 5 km, and, in particular, small magnitude events, in the range 4.0-4.6, are well sampled even at smaller distances. Only records at distances greater than 10 km are available for the two earthquakes with magnitude larger than 6,i.e. the 1976 Friuli (id = 2 in Table 1) and the 1980 Irpinia (id = 26 in Table 1).

Figure 3 shows the comparison between the PGA and Rjb used in ITACA and those for common records considered by SP87. While the PGA are similar, indicating that the different data processing resulted in consistent results, significant deviations are observed in the Rjb values for distances smaller than 20 km. These difference are likely to due to the improvement in the identification of seismogenic source geometries for Italian earthquakes with magnitude larger than 5.5 (DISS working group, 2006). Finally, the three site classes are sampled as follows: 104 waveforms belong to category C0, 47 to category C1 and 55 to C2, respectively, while about 50% of the events (53) have a normal-slip mechanism.

3. Model

The GMPEs are developed considering the following functional (e.g. Akkar and Bommer, 2007):

(1)

where Y is the response variable; Mref is a reference magnitude; R is the distance; h is the pseudo-depth (km); Si with i=1,2,3 are dummy variables that assume either the value 0 or 1 depending on soil type (rock, class C0: S1=1 and S2=S3=0; shallow alluvium, class C1: S2=1 and S1=S3=0; deep alluvium, class C2: S3=1 and S1=S2=0); Fj are dummy variables that take either the value 0 or 1 depending on the style of faulting (normal fault: F1=1 and F2=F3=0; strike-slip: F2=1 and F1=F3=0; reverse fault: F3=1 and F1=F2=0); ei and fj are the site and the style-of-faulting coefficients, respectively. Two different set of regressions were performed, considering either the epicentral distance (Repi) or considering Rjb for M≥5.5 and Repi for smaller magnitudes. A regression scheme based on the random effect model (Brillinger and Preisler, 1985; Abrahmson and Youngs, 1992) was adopted to describe the errors which are assumed to be independent and normally distributed. The variability of the errors for different stations that recorded the same event is the inter-event term (eve) while the variability of the errors for different earthquakes recorded by the same station is the inter-station term (sta), as described by Bindi et al. (2006). The regressions were performed for the maximum horizontal (maxH) and vertical peak ground (V) acceleration (PGA) and velocity (PGV), as well as for 5%-damped spectral acceleration (SA) at 21 periods from 0.03 to 2 sec. The reference magnitude Mref was fixed to 4.5.

4. Results

The regressions coefficients of equation (1) were derived twice, considering or neglecting the style-of-faulting parameter. In the former case, the coefficient fj for the normal slip earthquakes was assumed as reference and constrained to zero. Since the regression accounting for the style of faulting provided coefficients fj not significantly different from zero, and their introduction did not significantly reduced the variance of the residuals, only the results obtained without including the style of faulting are further considered. The results of this study will be hereinafter referred to as ITA08.

Tables 2a and 2b list the coefficients obtained for the maximum horizontal and the vertical components for peak ground acceleration and velocity considering the Joyner-Boore and epicentral distance, respectively. The coefficients obtained for the 5% damped acceleration response spectra are listed in Tables 3a and 3b  for maxH and in Tables 4a and 4b for the vertical component. Figure 4 shows the site coefficients versus period considering the maxH spectral accelerations. The site coefficient for class C1 is larger than 0.2 for periods smaller than 0.2s whereas class C2 is characterized by amplifications at periods larger than 0.4s. This result confirms that the adopted site classification scheme mainly discriminates between sub-surface geological conditions that led to local site amplification effects either in the low or in the high frequency range, being the transition zone over the 2.5 -5 Hz frequency range.

Considering Rjb, the total standard deviation varies between 0.3523 and 0.3659 for maxH and 0.3288 and 0.3384 for the vertical component. These values are significantly larger than those evaluated in SP96 (for horizontal components 0.173 and 0.215 for PGA and PGV, respectively), which are, in turn, much smaller than typical GMPE sigma’s derived worldwide (generally in the range 0.3 - 0.4). Bindi et al. (2009) recalculated the coefficients of the functional form used by Sabetta and Pugliese (1987, 1996) enlarging their data set with the recordings of the strongest earthquakes occurred after 1984 (M > 5.3) and obtained standard deviations equal to 0.3 and 0.31 for maximum horizontal PGA and PGV, respectively. This result confirms that the standard deviations of the GMPEs developed by Sabetta and Pugliese (1987, 1996) underestimate the observed ground motion variability when simple predictive models and site classification scheme are considered.

Figure 5 shows the distributions of inter-event variability and inter-station variability for the maximum horizontal and vertical component of PGA. Most of the inter-event errors vary in the range from -0.2 and 0.2. Only some events have significant errors (e.g. Molise 2002), caused by the strong overestimation or underestimation of the predictions. The inter-station variability is the dominant component of variance for both horizontal PGA and PGV (sta in Tables 2a,b) but the dominancy of sta diminishes with increasing periods (Tables 3a,b). For the vertical component (Tables 2a,b and 4a,b), the inter-event standard deviation is larger than the inter-station one, confirming that the vertical component of ground motion is generally less affected by local site amplification effects.

Figures from 6 to 8 show the attenuation of horizontal PGA and PGV with distances, comparing the GMPE obtained in this study with global predictive models valid for Europe or worldwide. The comparisons are made for rock sites, for the difficulties in comparing the soil classes of the different predictive models.

Figure 6 shows the attenuation of horizontal PGA and PGV with distances and a comparison with the European models developed by Ambraseys et al (2005) and Akkar and Bommer (2007) (hereinafter referred to as Amb05 and AkBo07, respectively, whose main characteristics are listed in Table 5). Three magnitude values are considered: 5, 6 and 6.9, and the mean plus or minus one standard deviation is plot using bands of different colours. Different symbols are used for the observations, accordingly to the style of faulting. Since the considered data set does not sample distances smaller than 10km for magnitudes larger than 6, the comparison for the 6.9 earthquake (Irpinia earthquake) is reliable only for distances >10 km (the ITA08 curves over distances <10 km are plotted with dashed lines). For both PGA and PGV, a good agreement with Amb05 and AkBo07 is observed for distances greater than 10km. For distances smaller than 10km, the predictions of ITA08 underestimate those obtained from the European model by a factor up to 2 for both PGA and PGV. Moreover, Amb05 and AkBo07 show smaller dispersion around the mean than ITA08 since their standard deviations are function of magnitude, increasing with decreasing magnitude . Figure 7 shows the mean curve proposed in this study (ITA08) and the mean plus or minus one standard deviation derived by AkBo07 and by Boore and Atkinson (2008) (hereinafter referred to as BAT08). The predictions from BAT08 are computed setting the Vs,30 value to 760 m/s, the threshold value which separates class A (hard rock) from B (rock)in the NEHRP soil classification. At short distances, the ITA08 predictions are between the mean and the mean minus one standard deviation of BAT08, although our data set is poorly sampled at magnitudes greater than 6 (Figure 2) and 6.9 is the upper magnitude limit of ITA08. For distances larger than 10 km, ITA08 shows a good agreement with AKB07.

The comparison between ITA08 and the SP96 models is shown in Figures 8 and 9 for PGA and PGV, considering three different magnitudes. The mean plus or minus one standard deviation is plot using bands of different grey levels. The main differences are in the magnitude dependence of geometrical spreading, not taken into account by SP96, and in the value of the standard deviation. In particular, a strong over-estimation at large distance is observed with respect to ITA08, in particular for magnitude 5.

. The standard deviations of the horizontal component are generally high (> 0.35) and the highest values are found for periods larger than 1s (about 0.39 - 0.40). Vertical components have lower standard deviations than the horizontal, although an increase is observed for periods greater than 0.7s. Table 3a confirms that sta is the dominant component of variability for the horizontal components, with the largest values observed for period between 0.07 s and 0.2s (i.e., frequencies between 5 and 14 Hz).

Figure 10 compares the horizontal spectral acceleration predicted by ITA08 with the Amb05 predictions for rock sites and normal fault, as the majority of earthquakes in Italy are generated by extensional tectonics. For magnitude 6.5, a good agreement is observed at both 20 and 50 km while for magnitude 5.5 the predictions agree only at 20 km since at 50 km ITA08 predictions under-estimate Amb05 for periods greater than 0.15 s.

Finally, the results for the vertical components are expressed in terms of vertical-to-horizontal response spectra ratio (V/H). A recent study about the engineering characteristics of the vertical ground motion has been published by Bozorgnia and Campbell (2004). They observed that the V/H ratio is a strong function of natural period, source-to-site distance, and local site conditions; and a relatively weak function of magnitude and faulting mechanism. Moreover, the dependence of V/H on distance is much different for firm soil than for very firm soil, soft rock or firm rock. In particular, the largest values of V/H (up to a factor of 1.8) are obtained considering predictions for firm soil sites, at short periods, close distances, and large magnitudes. At small magnitudes and large distances, the only significant effect of site conditions observed by Bozorgnia and Campbell (2004) is the tendency for V/H to be higher on firm rock for periods exceeding 0.2 s. Further evidences about the V/H ratio for a recently developed GMPE can be found in Cauzzi and Faccioli (2008).

Figure 11 shows the V/H ratio predicted by the models derived in this study, for two different magnitudes (6.9 and 5.5) and two different distances (10 and 60km). Our ratios are compared to the curves proposed by Bozorgnia and Campbell (2004) for firm soil (corresponding to classes C1 and C2 of this work) and firm rock, soft rock and very firm soil (class C0 of this work). The trend of the ratios is consistent with the observations of Bozorgnia and Campbell (2004), characterized by a bump at short periods (< 0.2s) and an almost constant ratio at longer periods (> 0.3s). In particular, a remarkable amplification of the vertical component (ratio greater than 1) is observed for class C2 and magnitude 6.9 for periods lower than 0.1 s. The results in Figure 11 suggest that the V/H for class C1 is more similar to C0 than C2, both at short and long periods. Finally, our data set shows a dependence of V/H on the event magnitude more than what observed by Bozorgnia and Campbell (2004).

5. A posteriori validation of  GMPEs: the Mw 5.4 Parma earthquake (December, 23 2008)

On December 23, 2008 a Mw 5.4 earthquake occurred in the northern Apennines, close to the town of Parma. The mainshock (origin time 15:24:21 GMT) was followed by a Mw 4.9 (Ml = 4.7) earthquake (origin time 21:58:25 GMT). The two earthquakes have hypocentral depth larger than 20km and reverse focal mechanism. The mainshock was recorded by 33 strong-motion stations (20 belonging to RAN and 13 to RAIS with epicentral distances between 32 and 217km. The Mw 4.9 aftershock has been recorded by 26 strong-motion stations (15 belonging to RAN and 11 to RAIS) in the distance range 9 - 217km. The closest recording (epicentral distance 9.2 km) of the Mw 4.9 earthquake is related to a temporary station installed by INGV Milano-Pavia after the mainshock occurrence.

The occurrence of these earthquakes represents a good opportunity to validate the predictive equations proposed in this study, although a large number of stations that recorded the two events were installed after 2004 and they were not considered in the development of the GMPE presented in this study. Moreover, as shown in Figure 2, these events are characterized by Mw values that are well sampled in the data-set used for the GMPE, both in terms of number of records and distance distribution. It is worth noting that in the last 30 years Italy suffered several moderate earthquakes (5 ( M ( 5.5) which, due to the high degree of vulnerability of many ancient historical villages (Central and Southern Italy) or to the high-rate of industrial facilities (Northern Italy), produced large damages and losses (e.g, the Mw 5.5, 31 October 2002, San Giuliano di Puglia earthquake or the Mw 5.3, 24 November 2004 Salò earthquake).

The data were processed following the same procedure adopted for ITACA (for details see Massa et al., 2009, this issue); Figure 12 shows that the acceleration response spectra ordinates calculated for the Parma earthquakes at the period of 0.1s, 0.5s, and 1s fit those reported in ITACA.

In order to check the improvements of ITA08 with respect to previous studies, we compare the observations of the Parma earthquakes (both in term of PGA and PGV) to ITA08 and SP96 predictions. Since detailed geological and geophysical information on the recording stations are currently not available, the comparisons are done only qualitatively, by comparing the mean prediction for rock conditions ( ( 1σ) to the observations classified as rock and soil.

Figure 13 shows that both ITA08 and SP96 fit the data recorded at station NEVI with distance 10km. On the contrary, for distances larger than 30km, SP96 overestimates the observations both in terms of acceleration and velocity. As the SP96 functional form does not include the magnitude dependent geometrical spreading, the discrepancies increase with increasing distances. When the Mw 4.9 earthquake is considered the differences with SP96 increases probably as the magnitude of this earthquake (Ml = 4.7) is close to the lowest magnitude threshold of SP96 (Ml = 4.6).

On the other hand, figure 13 shows that, for almost all stations, the observations are included in the ITA08 ( 1σ. Some recordings of the Mw 5.4 earthquake at distances between 30 and 60 km deserve further investigations as strong discrepancies (over-estimation of the predictions up to one order of magnitude) are observed for several rock sites. The sparse trend of rock and soil sites highlights that a reliable site classification is not currently available.

Finally, figure 14 shows the good agreement between ITA08 predictions and observations for spectral acceleration (damping 5%) at the three different periods (0.3s, 1.0s, 2.0s) used in Italy for the computation of the ShakeMaps.

5. Conclusions

The recordings of the new Italian Strong Motion Archive (ITACA) and the RAIS network database were considered to derive empirical ground motion prediction equations for Italy (ITA08). A larger and more qualified data set than the one used by Sabetta and Pugliese (1987 and 1996) was exploited for the regression. The data set qualification was performed through the event relocation, a careful magnitude attribution and the characterization of the recording sites using geological, geophysical and geotechnical investigations and recent seismological studies. The GMPE functional form has been changed respect to SP96 models, including a quadratic term in magnitudeand a magnitude dependence of the geometrical spreading. The results of this study show remarkable differences with the SP96 and an agreement, for distances larger than 10 km, with recently proposed GMPEs (Ambraseys et al., 2005 and Akkar and Bommer, 2007). At distances shorter than 10 km, the underestimation of ITA08 with respect to the European models can be attributed to the scarce data sampling over the short-distance range.

The future developments will be addressed to the improvement of the site classification scheme, which can exploit the results of an ongoing project named “Italian Accelerometric Database”, funded by the Italian Civil Protection (http://esse4.mi.ingv.it), whose aim is to acquire a relevant number of shear wave velocity profiles at different sites in Italy. Recent papers have proposed soil classification alternative to the SP96 scheme, based on quantitative parameters, such as the mean shear wave velocity profile at different depths or the fundamental frequency of resonance of the site. We believe that a new soil classification may reduce the GMPE standard deviation, as the inter-station error represents a large component of the variability.

Acknowledgments

This work has been carried out within the DPC-INGV S4 (2007-2009) project, funded by the Italian Department of Civil Protection (DPC) and developed in agreement with the Italian National Institute for Geophysics and Vulcanology (INGV). The authors thank G. Ameri for useful discussions that improved the manuscript. Comments and suggestions from S. Akkar and R. Paolucci are strongly acknowledged

References

Abrahamson NA, Youngs RR (1992) A stable algorithm for regression analyses using the random effects model. Bull Seism Soc Am 82:505–510.

Ambraseys NN, Douglas J, Sarma SK, Smit PM (2005) Equations for estimation of strong ground motions from shallow crustal earthquakes using data from Europe and the Middle East: horizontal peak ground acceleration and spectral acceleration. Bull. Earth. Eng. 3: 1-53.

Akkar S, Bommer JJ (2007) Empirical Prediction Equations for Peak Ground Velocity Derived from Strong-Motion Records from Europe and the Middle East. Bull Seism Soc Am 97 (2): 511-530.

Basili R, Valensise G, Vannoli P, Burrato P, Fracassi U, Mariano S, Tiberti MM, Boschi E (2008) The Database of Individual Seismogenic Sources (DISS), version 3: Summarizing 20 years of research on Italy's earthquake geology. Tectonophysics 453: 20-43, DOI: 10.1016/j.tecto.2007.04.014.

Bindi D, Luzi L, Pacor F, Franceschina G, Castro RR (2006) Ground-Motion Prediction from Empirical Attenuation Relationships versus Recorded Data: The Case of the 1997-1998 Umbria-Marches, Central Italy, Strong Motion Data Set. Bull Seism Soc Am 96 (3): 984-1002.

Bindi D, Luzi L, Pacor F, Sabetta F, Massa M (2009) Towards a new reference ground motion prediction equation for Italy: update of the Sabetta-Pugliese (1996) ground motion prediction equations. Bulletin of Earthquake Engineering, in press

Boore DM, Atkinson GM (2008) Ground motion prediction equations for the mean horizontal component of PGA, PGV and 5%-damped PSA at spectral periods between 0.01 s and 10.0 s. Earthquake Spectra 24 n.1: 99-138.

Bozorgnia Y, Campbell KW (2004) The vertical to horizontal response spectral ratio and tentative procedures for developing simplified V/H and vertical design spectra. Journal of Earth Eng 8(2): 175-207.

Bragato PL, Slejko D (2005) Empirical ground-motion attenuation relations for the Eastern Alps in the magnitude range 2.5-6.3. Bull Seism Soc Am 95(1): 252-276.

Brillinger DR, Preisler HK (1985) Further analysis of the Joyner-Boore attenuation data. Bull Seism Soc Am 75: 611–614.

Cauzzi C and Faccioli E (2008) Broadband (0.05 to 20s) prediction of displacement response spectra based on worldwide digital records. J.Seismol. DOI 10.1007/s10950-008-9098-y.

Cornell CA (1968) Engineering seismic risk analysis. Bull Seism Soc Am 58: 1583-1606.

DISS Working Group (2006) Database of Individual Seismogenic Sources (DISS), Version 3.0.2: A compilation of potential sources for earthquakes larger than M 5.5 in Italy and surrounding areas. http://www.ingv.it/DISS/, © INGV 2005, 2006 - Istituto Nazionale di Geofisica e Vulcanologia - All rights reserved.

Frisenda M, Massa M, Spallarossa D, Ferretti G, Eva C (2005) Attenuation relationship for low magnitude earthquakes using standard seismometric records. Journal of Earth Eng 9(1): 23-40.

Luzi L, Hailemikael S, Bindi D, Pacor F, Mele F (2008) ITACA (ITalian ACcelerometric Archive): a web portal for the dissemination of Italian strong motion data. Seism. Res. Lett. Doi:10.1785/gssrl.79.5.

Massa M, Morasca P, Moratto L, Marzorati S, Costa G, Spallarossa D (2008) Empirical ground motion prediction equations for Northern Italy using weak and strong motion amplitudes, frequency content and duration parameters. Bull Seism Soc Am 98(3): 1319-1342.

Massa M, Pacor F, Luzi L, Bindi D, Milana G, Sabetta F, Gorini A, Marcocci C. (2008) The Italian Accelerometric Archive (ITACA): data processing. Bull of Earth Eng (this issue).

Sabetta F, Pugliese A (1987) Attenuation of peak horizontal acceleration and velocity from Italian strong-motion records. Bull Seism Soc Am 77: 1491-1513.

Sabetta F, Pugliese A (1996) Estimation of response spectra and simulation of non-stationary earthquake ground motions. Bull Seism Soc Am 86(2): 337-352.

Figure and table captions

Figure 1. Left: geographic distribution of recording stations, right: geographic distribution of earthquakes.

Figure 2. Magnitude versus distance distribution (different symbol indicate soil classes).

Figure 3. Left: comparison between the PGA (in cm/s2) computed by Sabetta and Pugliese (1987) and those used in the study (PGA-ITACA). Right: comparisons between the Joyner-Boore distance used by Sabetta and Pugliese (1987) and those considered in this study.

Figure 4. Site coefficients (see equation 1) for classes C1 (shallow alluvium) and C2 (deep alluvium) for maxH spectral acceleration as function of period (s).

Figure 5. Inter-event (top panels) and inter-station (bottom panels) distribution of errors for PGA, considering the maximum horizontal (left side) and vertical components (right side).

Figure 6. PGA (left) and PGV (right) versus distances for rock sites and three different magnitudes: 6.9 (upper panel), 6 (middle panel) and 5 (bottom panel).

Figure 7. Comparison between ITA08, Boore and Atkinson (2008) and Akkar and Bommer (2007) for peak ground velocity and rock sites.

Figure 8. Comparison between ITA08 and SP96 models for PGA (left) and PGV (right), rock sites and three magnitudes 6.9 (upper panel), 6 (middle panel) and 5 (bottom panel). The Joyner-Boore distance is considered.

Figure 9. The same as Figure 8 but considering the epicentral distance

Figure 10. Comparison between 5% damped acceleration spectra obtained with (ITA08) and Amb05: magnitudes 6.5 and 5.5 at 20 km (left) and magnitudes 6.5 and 5.5 at 50 km (right).

Figure 11. Vertical-to-horizontal response spectra ratio (V/H) for magnitudes 6.9 (distance 10km and 60km) and magnitude 5.5 (distance 10km and 60km) for rock sites (top panel), shallow alluvium (middle panel) and deep alluvium (bottom panel); black solid lines are the reference curves in Bozorgnia and Campbell (2004).

Figure 12. Acceleration response spectra (SA) ordinates for the events included in ITACA (black circles) and for the Mw 5.4 Parma earthquake (grey circles).

Figure 13. Parma earthquake records  compared to ITA08 (left panels) and SP96 (right panels) mean predictions for rock sites (black lines). White circles rock sites (C0 class), grey circles indicate soil sites (C1 and C2 classes). Light grey areas represent the ITA08 standard deviation.

Figure 14. Comparison between observed (circles) acceleration response spectra ordinates (damping 5%) computed for the Parma earthquakes (Mw=5.4 on the left and Mw=4.9 on the right) and ITA08 predictions (black lines) for periods of 0.3s, 1.0s and 2.0s. White circles indicate rock sites (C0 class), grey circles indicate soil sites (C1 and C2 classes). Light grey areas represent the ITA08 standard deviation.

Table 1. Characteristics of the selected seismic events (Id = earthquake index; Lon = longitude; Lat = latitude; Mech = focal mechanism: 1=normal, 2 =reverse, 3=strike-slip, 4 =unknown).

Table 2a. Coefficient for the prediction of horizontal and vertical PGA (cm/s2) and PGV (cm), considering the Joyner-Boore distance.

Table 2a. Coeffibient for the prediction of horizontal and vertical PGA (cm/s2) and PGV (cm), considering the epicentral distance.

Table 3a. Coefficient for the prediction of horizontal 5% damped acceleration response spectra (cm/s2), considering the Joyner-Boore distance.

Table 3b. Coefficient for the prediction of horizontal 5% damped acceleration response spectra (cm/s2), considering the epicentral distance.

Table 4a. Coefficient for the prediction of vertical 5% damped acceleration response spectra (cm/s2), considering the Joyner-Boore distance.

Table 4b. Coefficient for the prediction of vertical 5% damped acceleration response spectra (cm/s2), considering the epicentral distance.

Table 5. Characteristics of the GMPEs used in this study (Nrec, Neve = number of records, number of events; Mrange = magnitude range; Rmin, Rmax = minimum diatnce, maximum distance (km); Site class = number of site classes used; Component L = larger, G = geometric mean, GMRot = geometric mean determined from the 50th percentile values of the geometric means computed for all non-redundant rotation angles and all periods less than the maximum useable period).

Figure 1

Figure 2

Figure 3.

Figure 4.

Figure 5

Figure 6

Figure 7

Figure 8

Figure9

Figure 10

Figure 11

=

Figure 12

Figure 13

Figure 14

Table 1.

| Id | Year | Month | Day | Hour (GMT) | Lon | Lat | Depth (km) | Mw | Mech |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 1972 | 06 | 14 | 18:55:46 | 13.600 | 43.650 | 3.00 | 4.8 | 3 |
| 2 | 1976 | 05 | 06 | 20:00:12 | 13.260 | 46.350 | 12.00 | 6.4 | 2 |
| 3 | 1976 | 05 | 09 | 00:53:44 | 13.320 | 46.220 | 20.00 | 5.1 | 2 |
| 4 | 1976 | 05 | 10 | 04:35:53 | 13.120 | 46.260 | 15.00 | 4.7 | 2 |
| 5 | 1976 | 05 | 11 | 22:44:00 | 12.990 | 46.290 | 13.00 | 5.0 | 2 |
| 6 | 1976 | 05 | 13 | 13:04:50 | 12.983 | 46.233 | 16.00 | 4.1 | 1 |
| 7 | 1976 | 05 | 18 | 01:30:08 | 12.867 | 46.250 | 5.00 | 4.1 | 1 |
| 8 | 1976 | 06 | 01 | 17:21:07 | 12.867 | 46.217 | 15.00 | 4.1 | 1 |
| 9 | 1976 | 06 | 08 | 12:14:38 | 13.230 | 46.300 | 19.00 | 4.6 | 1 |
| 10 | 1976 | 06 | 09 | 18:48:15 | 13.067 | 46.350 | 16.00 | 4.3 | 1 |
| 11 | 1976 | 06 | 17 | 14:28:47 | 12.798 | 46.177 | 15.00 | 4.7 | 1 |
| 12 | 1976 | 09 | 07 | 11:08:16 | 12.983 | 46.300 | 5.00 | 4.2 | 1 |
| 13 | 1976 | 09 | 11 | 16:31:10 | 13.180 | 46.290 | 10.00 | 5.1 | 2 |
| 14 | 1976 | 09 | 11 | 16:35:01 | 13.320 | 46.300 | 9.00 | 5.6 | 2 |
| 15 | 1976 | 09 | 15 | 03:15:18 | 13.190 | 46.300 | 2.00 | 5.9 | 2 |
| 16 | 1976 | 09 | 15 | 04:38:53 | 13.170 | 46.270 | 21.00 | 4.9 | 1 |
| 17 | 1976 | 09 | 15 | 09:21:18 | 13.180 | 46.300 | 21.00 | 5.9 | 2 |
| 18 | 1977 | 04 | 03 | 03:18:13 | 13.100 | 46.267 | 9.00 | 4.8 | 2 |
| 19 | 1977 | 09 | 16 | 23:48:07 | 12.980 | 46.280 | 21.00 | 5.3 | 2 |
| 20 | 1978 | 03 | 11 | 19:20:43 | 16.184 | 37.979 | 5.00 | 5.2 | 1 |
| 21 | 1978 | 04 | 15 | 23:33:47 | 15.110 | 38.270 | 22.00 | 6.0 | 3 |
| 22 | 1979 | 09 | 19 | 21:35:37 | 13.040 | 42.800 | 6.00 | 5.8 | 1 |
| 23 | 1980 | 02 | 28 | 21:04:40 | 12.967 | 42.800 | 12.00 | 5.0 | 4 |
| 24 | 1980 | 05 | 14 | 09:01:13 | 13.000 | 42.855 | 15.00 | 4.1 | 4 |
| 25 | 1980 | 06 | 09 | 16:02:47 | 13.860 | 42.246 | 12.00 | 4.6 | 1 |
| 26 | 1980 | 11 | 23 | 18:34:53 | 15.310 | 40.760 | 15.00 | 6.9 | 1 |
| 27 | 1980 | 11 | 24 | 00:24:00 | 15.268 | 40.811 | 13.00 | 5.0 | 1 |
| 28 | 1980 | 11 | 25 | 17:06:44 | 15.462 | 40.609 | 18.00 | 5.0 | 1 |
| 29 | 1980 | 11 | 30 | 07:41:59 | 15.316 | 40.761 | 18.00 | 4.5 | 4 |
| 30 | 1980 | 12 | 01 | 19:04:29 | 15.310 | 40.890 | 9.00 | 4.6 | 4 |
| 31 | 1980 | 12 | 04 | 00:04:56 | 15.527 | 40.746 | 12.00 | 4.0 | 4 |
| 32 | 1980 | 12 | 08 | 02:49:39 | 15.231 | 40.821 | 13.00 | 4.2 | 4 |
| 33 | 1980 | 12 | 08 | 04:09:24 | 15.249 | 40.785 | 14.00 | 4.1 | 4 |
| 34 | 1981 | 01 | 16 | 00:37:45 | 15.440 | 40.840 | 10.47 | 5.2 | 1 |
| 35 | 1981 | 02 | 14 | 17:27:46 | 14.794 | 41.060 | 10.10 | 4.9 | 2 |
| 36 | 1982 | 10 | 17 | 06:45:37 | 12.714 | 43.162 | 5.90 | 4.6 | 1 |
| 37 | 1984 | 04 | 29 | 05:03:00 | 12.570 | 43.210 | 5.97 | 5.6 | 1 |
| 38 | 1984 | 05 | 07 | 17:49:43 | 13.860 | 41.700 | 20.50 | 5.9 | 1 |
| 39 | 1984 | 05 | 11 | 10:41:48 | 13.890 | 41.780 | 12.10 | 5.5 | 1 |
| 40 | 1984 | 05 | 11 | 11:26:15 | 13.885 | 41.705 | 13.60 | 4.1 | 4 |
| 41 | 1984 | 05 | 11 | 13:14:56 | 13.919 | 41.754 | 12.20 | 4.8 | 1 |
| 42 | 1984 | 05 | 11 | 23:35:04 | 13.883 | 41.678 | 8.80 | 4.0 | 4 |
| 43 | 1985 | 01 | 23 | 10:10:17 | 10.415 | 44.064 | 24.10 | 4.7 | 4 |
| 44 | 1985 | 05 | 20 | 10:00:29 | 13.372 | 42.266 | 11.50 | 4.2 | 4 |
| 45 | 1987 | 04 | 24 | 02:30:29 | 10.674 | 44.816 | 23.50 | 4.9 | 3 |
| 46 | 1987 | 05 | 02 | 20:43:55 | 10.678 | 44.794 | 23.70 | 4.7 | 3 |
| 47 | 1987 | 07 | 05 | 13:12:37 | 12.208 | 43.759 | 15.50 | 4.4 | 1 |
| 48 | 1988 | 02 | 08 | 11:24:46 | 10.465 | 44.106 | 27.70 | 4.6 | 4 |
| 49 | 1990 | 05 | 05 | 07:21:20 | 15.860 | 40.640 | 22.54 | 5.8 | 3 |
| 50 | 1990 | 12 | 13 | 00:24:26 | 15.320 | 37.270 | 7.00 | 5.6 | 3 |
| 51 | 1991 | 01 | 14 | 07:38:36 | 11.891 | 43.828 | 14.20 | 4.0 | 4 |
| 52 | 1995 | 09 | 30 | 10:14:34 | 15.914 | 41.814 | 27.40 | 5.2 | 2 |
| 53 | 1996 | 04 | 03 | 13:04:35 | 15.442 | 40.655 | 11.40 | 4.9 | 1 |
| 54 | 1996 | 10 | 15 | 09:56:01 | 10.605 | 44.763 | 25.50 | 5.4 | 2 |
| 55 | 1996 | 10 | 20 | 19:06:56 | 13.263 | 42.559 | 11.90 | 4.4 | 1 |
| 56 | 1997 | 09 | 26 | 00:33:12 | 12.890 | 43.020 | 3.51 | 5.7 | 1 |
| 57 | 1997 | 09 | 26 | 09:40:25 | 12.850 | 43.010 | 9.87 | 6.0 | 1 |
| 58 | 1997 | 09 | 26 | 13:30:52 | 12.905 | 43.035 | 13.90 | 4.5 | 1 |
| 59 | 1997 | 09 | 27 | 17:13:03 | 12.812 | 43.011 | 6.70 | 4.2 | 1 |
| 60 | 1997 | 09 | 27 | 19:56:43 | 12.826 | 43.036 | 8.20 | 4.3 | 1 |
| 61 | 1997 | 10 | 02 | 10:59:56 | 12.778 | 43.105 | 8.20 | 4.7 | 1 |
| 62 | 1997 | 10 | 03 | 08:55:22 | 12.824 | 43.043 | 12.10 | 5.2 | 1 |
| 63 | 1997 | 10 | 04 | 15:07:20 | 12.918 | 42.917 | 5.10 | 4.4 | 1 |
| 64 | 1997 | 10 | 04 | 16:13:32 | 12.906 | 42.916 | 6.20 | 4.7 | 1 |
| 65 | 1997 | 10 | 04 | 18:47:47 | 12.904 | 42.924 | 6.10 | 4.4 | 1 |
| 66 | 1997 | 10 | 06 | 23:24:53 | 12.847 | 43.028 | 3.90 | 5.4 | 1 |
| 67 | 1997 | 10 | 07 | 01:24:34 | 12.846 | 43.037 | 4.90 | 4.2 | 1 |
| 68 | 1997 | 10 | 07 | 05:09:56 | 12.859 | 43.036 | 1.70 | 4.5 | 1 |
| 69 | 1997 | 10 | 12 | 11:08:36 | 12.920 | 42.906 | 0.10 | 5.2 | 1 |
| 70 | 1997 | 10 | 12 | 11:12:29 | 12.922 | 42.920 | 0.50 | 4.2 | 4 |
| 71 | 1997 | 10 | 14 | 15:23:09 | 12.900 | 42.900 | 7.33 | 5.6 | 1 |
| 72 | 1997 | 10 | 14 | 23:23:29 | 12.872 | 42.956 | 4.10 | 4.1 | 4 |
| 73 | 1997 | 10 | 16 | 12:00:31 | 12.884 | 43.044 | 2.40 | 4.3 | 3 |
| 74 | 1997 | 10 | 19 | 16:00:17 | 12.848 | 42.971 | 3.90 | 4.2 | 1 |
| 75 | 1997 | 11 | 08 | 15:31:53 | 12.974 | 42.863 | 0.30 | 4.1 | 4 |
| 76 | 1997 | 11 | 09 | 19:07:33 | 12.988 | 42.846 | 1.50 | 4.9 | 1 |
| 77 | 1997 | 11 | 30 | 11:24:42 | 12.990 | 42.842 | 3.50 | 4.0 | 1 |
| 78 | 1998 | 02 | 07 | 00:59:44 | 12.823 | 43.005 | 0.00 | 4.3 | 4 |
| 79 | 1998 | 04 | 03 | 07:26:36 | 12.757 | 43.185 | 1.90 | 5.1 | 1 |
| 80 | 1998 | 04 | 03 | 07:59:52 | 12.755 | 43.194 | 3.90 | 4.3 | 1 |
| 81 | 1998 | 04 | 05 | 15:52:21 | 12.767 | 43.190 | 4.40 | 4.8 | 1 |
| 82 | 1998 | 06 | 02 | 23:11:23 | 12.786 | 43.186 | 3.30 | 4.3 | 1 |
| 83 | 1998 | 08 | 15 | 05:18:08 | 13.056 | 42.362 | 2.90 | 4.4 | 1 |
| 84 | 1998 | 09 | 09 | 11:28:00 | 15.950 | 40.060 | 29.21 | 5.6 | 1 |
| 85 | 1999 | 01 | 25 | 22:45:58 | 11.962 | 43.980 | 27.90 | 4.4 | 3 |
| 86 | 1999 | 02 | 14 | 11:45:53 | 15.022 | 38.226 | 20.70 | 4.7 | 1 |
| 87 | 2000 | 12 | 16 | 07:31:07 | 12.586 | 42.516 | 9.20 | 4.2 | 1 |
| 88 | 2002 | 04 | 17 | 06:42:54 | 16.880 | 39.684 | 4.00 | 4.9 | 4 |
| 89 | 2002 | 10 | 27 | 02:50:27 | 15.106 | 37.766 | 0.00 | 4.9 | 3 |
| 90 | 2002 | 10 | 31 | 10:32:59 | 14.890 | 41.720 | 25.15 | 5.7 | 3 |
| 91 | 2002 | 11 | 01 | 15:09:02 | 14.840 | 41.740 | 21.36 | 5.7 | 3 |
| 92 | 2002 | 11 | 04 | 00:35:46 | 14.837 | 41.750 | 22.20 | 4.3 | 4 |
| 93 | 2002 | 11 | 04 | 03:26:30 | 14.823 | 41.764 | 21.10 | 4.0 | 4 |
| 94 | 2002 | 11 | 12 | 09:27:48 | 14.786 | 41.689 | 28.90 | 4.6 | 3 |
| 95 | 2003 | 01 | 26 | 19:57:04 | 11.936 | 43.892 | 5.80 | 4.7 | 1 |
| 96 | 2003 | 01 | 26 | 20:01:16 | 11.930 | 43.900 | 6.80 | 4.0 | 4 |
| 97 | 2003 | 06 | 01 | 15:45:18 | 14.825 | 41.666 | 16.20 | 4.8 | 2 |
| 98 | 2003 | 09 | 14 | 21:42:53 | 11.387 | 44.230 | 15.80 | 5.3 | 2 |
| 99 | 2003 | 12 | 07 | 10:20:33 | 12.138 | 44.159 | 19.60 | 4.2 | 2 |
| 100 | 2003 | 12 | 30 | 05:31:38 | 14.834 | 41.654 | 14.90 | 4.5 | 4 |
| 101 | 2004 | 03 | 03 | 02:13:26 | 15.160 | 39.815 | 2.30 | 4.6 | 4 |
| 102 | 2004 | 07 | 12 | 13:04:06 | 13.502 | 46.322 | 6.20 | 5.2 | 2 |
| 103 | 2004 | 09 | 03 | 00:04:13 | 15.646 | 40.681 | 10.10 | 4.1 | 4 |
| 104 | 2004 | 12 | 09 | 02:44:25 | 13.722 | 42.784 | 18.20 | 4.0 | 4 |
| 105 | 2006 | 10 | 20 | 00:11:12 | 10.360 | 45.720 | 5.00 | 4.2 | 4 |
| 106 | 2007 | 05 | 09 | 06:02:56 | 10.520 | 44.800 | 27.20 | 4.3 | 4 |
| 107 | 2007 | 07 | 30 | 19:05:04 | 10.030 | 44.890 | 27.80 | 4.5 | 4 |

Table 2a

| horizontal | a | b1 | b2 | c1 | c2 | h | C0 | C1 | C2 | eve | sta |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| PGA | 3.7691 | 0.0523 | -0.1389 | -1.9383 | 0.4661 | 10.1057 | 0 | 0.2260 | 0.1043 | 0.2084 | 0.2634 | 0.3523 |
| PGV | 2.574 | 0.0496 | -0.0982 | -2.0846 | 0.528273 | 10.4844 | 0 | 0.146221 | 0.2701 | 0.2314 | 0.2819 | 0.3659 |
| vertical |  |  |  |  |  |  |  |  |  |  |  |  |
| PGA | 3.2191 | 0.1631 | -0.0765 | -1.7613 | 0.3144 | 9.1688 | 0 | 0.1938 | 0.1242 | 0.2080 | 0.1859 | 0.3288 |
| PGV | 2.0127 | 0.1069 | -0.0619 | -1.9206 | 0.4622 | 10.2227 | 0 | 0.1126 | 0.1907 | 0.2270 | 0.1747 | 0.3384 |

Table 2b

| horizontal | a | b1 | b2 | c1 | c2 | h | C0 | C1 | C2 | eve | sta |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| PGA | 3.750 | 0.1180 | -0.1147 | -1.9267 | 0.4285 | 10.0497 | 0 | 0.2297 | 0.1022 | 0.2103 | 0.2666 | 0.3555 |
| PGV | 2.5830 | 0.0890 | -0.0771 | -2.0896 | 0.5106 | 10.5886 | 0. | 0.1496 | 0.2673 | 0.2344 | 0.2454 | 0.3707 |
| vertical |  |  |  |  |  |  |  |  |  |  |  |  |
| PGA | 3.2015 | 0.2482 | -0.0428 | -1.7514 | 0.2588 | 9.1513 | 0. | 0.1983 | 0.1230 | 0.1917 | 0.1877 | 0.3241 |
| PGV | 2.0141 | 0.1447 | -0.0405 | -1.9207 | 0.4443 | 10.3378 | 0. | 0.1165 | 0.1879 | 0.2309 | 0.1773 | 0.3442 |

Table 3a.

| T (s) | a | b1 | b2 | c1 | c2 | h | C0 | C1 | C2 | eve | sta |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 0.03 | 3.8802 | 0.0086 | -0.1287 | -1.9720 | 0.4710 | 10.5940 | 0 | 0.2176 | 0.0866 | 0.2083 | 0.2603 | 0.3521 |
| 0.04 | 3.8569 | 0.0395 | -0.1255 | -1.9300 | 0.4431 | 10.0362 | 0 | 0.2221 | 0.0764 | 0.2158 | 0.2656 | 0.3648 |
| 0.07 | 4.0050 | 0.0479 | -0.1232 | -1.9197 | 0.4212 | 10.2414 | 0 | 0.2082 | 0.0390 | 0.1999 | 0.2887 | 0.3649 |
| 0.10 | 4.0176 | 0.0619 | -0.1120 | -1.8599 | 0.3949 | 10.4222 | 0 | 0.2572 | 0.0580 | 0.2045 | 0.2970 | 0.3734 |
| 0.15 | 4.1000 | 0.0930 | -0.1330 | -1.8769 | 0.4125 | 10.7824 | 0 | 0.2631 | 0.0632 | 0.2099 | 0.2941 | 0.3832 |
| 0.20 | 4.0808 | 0.0633 | -0.1358 | -1.8833 | 0.4546 | 10.5949 | 0 | 0.2126 | 0.1212 | 0.2149 | 0.2840 | 0.3924 |
| 0.25 | 3.9805 | 0.1333 | -0.1418 | -1.8756 | 0.4318 | 10.2248 | 0 | 0.1618 | 0.1454 | 0.2090 | 0.2647 | 0.3815 |
| 0.30 | 3.9016 | 0.1224 | -0.1407 | -1.8908 | 0.4551 | 9.7928 | 0 | 0.1409 | 0.1630 | 0.2219 | 0.2446 | 0.3750 |
| 0.35 | 3.8185 | 0.1167 | -0.1366 | -1.8992 | 0.4740 | 9.4714 | 0 | 0.1289 | 0.1892 | 0.2430 | 0.2479 | 0.3842 |
| 0.40 | 3.6578 | 0.1583 | -0.1470 | -1.8521 | 0.4727 | 9.2690 | 0 | 0.1146 | 0.2190 | 0.2213 | 0.2291 | 0.3740 |
| 0.45 | 3.5972 | 0.1656 | -0.1342 | -1.8678 | 0.4665 | 9.3437 | 0 | 0.0946 | 0.2632 | 0.2215 | 0.2327 | 0.3744 |
| 0.50 | 3.5304 | 0.2035 | -0.1320 | -1.8728 | 0.4519 | 9.2842 | 0 | 0.0763 | 0.2741 | 0.2197 | 0.2300 | 0.3713 |
| 0.60 | 3.3531 | 0.2456 | -0.1181 | -1.8463 | 0.4414 | 9.0307 | 0 | 0.0539 | 0.2973 | 0.2360 | 0.2290 | 0.3732 |
| 0.70 | 3.2126 | 0.2754 | -0.1209 | -1.8299 | 0.4396 | 8.8794 | 0 | 0.0447 | 0.3217 | 0.2379 | 0.2311 | 0.3761 |
| 0.80 | 3.0980 | 0.2949 | -0.0963 | -1.8318 | 0.4255 | 8.7481 | 0 | 0.0436 | 0.3406 | 0.2375 | 0.2308 | 0.3756 |
| 0.90 | 3.0472 | 0.3500 | -0.0952 | -1.8627 | 0.3992 | 9.1414 | 0 | 0.0400 | 0.3663 | 0.2393 | 0.2302 | 0.3784 |
| 1.00 | 3.0311 | 0.3555 | -0.0962 | -1.9011 | 0.4036 | 9.6044 | 0 | 0.0347 | 0.3791 | 0.2471 | 0.2560 | 0.3907 |
| 1.25 | 2.8210 | 0.3621 | -0.0963 | -1.8780 | 0.4151 | 9.5829 | 0 | 0.0233 | 0.4091 | 0.2605 | 0.2619 | 0.4119 |
| 1.50 | 2.8348 | 0.2498 | -0.1103 | -1.9787 | 0.5216 | 9.9923 | 0 | -0.0006 | 0.4111 | 0.2223 | 0.2654 | 0.4059 |
| 1.75 | 2.8610 | 0.1834 | -0.1040 | -2.0899 | 0.5880 | 10.8928 | 0 | -0.0002 | 0.4133 | 0.2359 | 0.2390 | 0.3987 |
| 2.00 | 2.7506 | 0.2056 | -0.1139 | -2.0976 | 0.5953 | 10.5615 | 0 | -0.0065 | 0.3836 | 0.2242 | 0.2112 | 0.3790 |

Table 3b

| T (s) | a | b1 | b2 | c1 | c2 | h | C0 | C1 | C2 | eve | sta |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 0.03 | 3.8636 | -0.0723 | -0.1043 | 1.9618 | 0.4346 | 10.5707 | 0. | 0.2211 | 0.0842 | 0.2102 | 0.2638 | 0.3553 |
| 0.04 | 3.8461 | 0.1056 | -0.0993 | -1.9232 | 0.4040 | 10.0637 | 0. | 0.2260 | 0.0742 | 0.2177 | 0.2690 | 0.3680 |
| 0.07 | 3.9944 | 0.1111 | -0.0962 | -1.9128 | 0.3835 | 10.2906 | 0. | 0.2122 | 0.0367 | 0.2017 | 0.2926 | 0.3682 |
| 0.10 | 3.9926 | 0.1360 | -0.0839 | -1.8447 | 0.3492 | 10.3528 | 0. | 0.2609 | 0.0560 | 0.2059 | 0.2781 | 0.3759 |
| 0.15 | 4.0596 | 0.1713 | -0.1061 | -1.8525 | 0.3646 | 10.6030 | 0. | 0.2667 | 0.0610 | 0.2114 | 0.2971 | 0.3859 |
| 0.20 | 4.0725 | 0.1252 | -0.1124 | -1.8780 | 0.4187 | 10.6263 | 0. | 0.2158 | 0.1191 | 0.2164 | 0.2859 | 0.3951 |
| 0.25 | 3.9793 | 0.1856 | -0.1177 | -1.8747 | 0.4025 | 10.3088 | 0. | 0.1654 | 0.1431 | 0.2108 | 0.2671 | 0.3849 |
| 0.30 | 3.8899 | 0.1709 | -0.1186 | -1.8837 | 0.4298 | 9.7877 | 0. | 0.1448 | 0.1605 | 0.2247 | 0.2474 | 0.3798 |
| 0.35 | 3.8082 | 0.1670 | -0.1153 | -1.8929 | 0.4480 | 9.4708 | 0. | 0.1329 | 0.1868 | 0.2244 | 0.2506 | 0.3794 |
| 0.40 | 3.6486 | 0.2120 | -0.1262 | -1.8463 | 0.4439 | 9.2789 | 0. | 0.1185 | 0.2168 | 0.2237 | 0.2314 | 0.3782 |
| 0.45 | 3.5930 | 0.2225 | -0.1119 | -1.8654 | 0.4352 | 9.3832 | 0. | 0.0983 | 0.2612 | 0.2239 | 0.2146 | 0.3784 |
| 0.50 | 3.5320 | 0.2612 | -0.1081 | -1.8738 | 0.4193 | 9.3706 | 0. | 0.0802 | 0.2722 | 0.2220 | 0.2322 | 0.3753 |
| 0.60 | 3.3660 | 0.3051 | -0.0931 | -1.8534 | 0.4061 | 9.2463 | 0. | 0.0581 | 0.2955 | 0.2391 | 0.2121 | 0.3781 |
| 0.70 | 3.2342 | 0.3272 | -0.0968 | -1.8420 | 0.4096 | 9.1689 | 0. | 0.0489 | 0.3197 | 0.2412 | 0.2141 | 0.3813 |
| 0.80 | 3.1072 | 0.3532 | -0.0708 | -1.8367 | 0.3911 | 8.9420 | 0. | 0.0481 | 0.3387 | 0.2409 | 0.2138 | 0.3809 |
| 0.90 | 3.0662 | 0.4113 | -0.0663 | -1.8733 | 0.3612 | 9.4254 | 0. | 0.0445 | 0.3645 | 0.2429 | 0.2333 | 0.3840 |
| 1.00 | 3.0468 | 0.4210 | -0.0666 | -1.9096 | 0.3627 | 9.8637 | 0. | 0.0389 | 0.3772 | 0.2504 | 0.2386 | 0.3959 |
| 1.25 | 2.8175 | 0.4168 | -0.0708 | -1.8762 | 0.3838 | 9.6593 | 0. | 0.0285 | 0.4079 | 0.2402 | 0.2444 | 0.4059 |
| 1.50 | 2.8253 | 0.2885 | -0.0923 | -1.9731 | 0.5055 | 9.9835 | 0. | 0.0035 | 0.4089 | 0.2249 | 0.2477 | 0.4106 |
| 1.75 | 2.8399 | 0.2188 | -0.0878 | -2.0782 | 0.5756 | 10.7942 | 0. | 0.0041 | 0.4124 | 0.2161 | 0.2424 | 0.3946 |
| 2.00 | 2.7171 | 0.2378 | -0.0990 | -2.0787 | 0.5868 | 10.3772 | 0. | -0.0012 | 0.3830 | 0.2058 | 0.1947 | 0.3758 |

Table 4a.

| T (s) | a | b1 | b2 | c1 | c2 | h | C0 | C1 | C2 | eve | sta |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 0.03 | 3.3378 | 0.1061 | -0.0626 | -1.7927 | 0.3214 | 9.3650 | 0 | 0.1974 | 0.1137 | 0.1928 | 0.1881 | 0.3259 |
| 0.04 | 3.2871 | 0.1978 | -0.0567 | -1.7169 | 0.2462 | 8.2612 | 0 | 0.2320 | 0.1198 | 0.1865 | 0.1789 | 0.3405 |
| 0.07 | 3.4305 | 0.2591 | -0.0558 | -1.6801 | 0.1938 | 8.2858 | 0 | 0.2066 | 0.1146 | 0.2099 | 0.2168 | 0.3548 |
| 0.10 | 3.4767 | 0.2962 | -0.0617 | -1.6467 | 0.1851 | 8.9225 | 0 | 0.1595 | 0.0933 | 0.2046 | 0.2129 | 0.3458 |
| 0.15 | 3.4249 | 0.3236 | -0.0906 | -1.6218 | 0.2165 | 9.7569 | 0 | 0.1766 | 0.1149 | 0.1999 | 0.2220 | 0.3378 |
| 0.20 | 3.5314 | 0.2441 | -0.0916 | -1.7322 | 0.2836 | 10.3065 | 0 | 0.1415 | 0.1378 | 0.2055 | 0.2118 | 0.3474 |
| 0.25 | 3.3264 | 0.2703 | -0.1016 | -1.6627 | 0.2930 | 9.3620 | 0 | 0.1329 | 0.1402 | 0.1996 | 0.1909 | 0.3375 |
| 0.30 | 3.2307 | 0.2704 | -0.0908 | -1.6443 | 0.2993 | 8.8936 | 0 | 0.0797 | 0.1296 | 0.2160 | 0.1910 | 0.3415 |
| 0.35 | 3.1481 | 0.2724 | -0.0938 | -1.6320 | 0.3057 | 9.1088 | 0 | 0.0854 | 0.1396 | 0.2074 | 0.1688 | 0.3279 |
| 0.40 | 3.0705 | 0.2682 | -0.0953 | -1.6377 | 0.3255 | 8.9782 | 0 | 0.0805 | 0.1582 | 0.2338 | 0.1567 | 0.3485 |
| 0.45 | 3.0589 | 0.2673 | -0.0994 | -1.6704 | 0.3488 | 9.3007 | 0 | 0.0481 | 0.1709 | 0.2414 | 0.1829 | 0.3599 |
| 0.50 | 3.0721 | 0.2918 | -0.0951 | -1.7171 | 0.3410 | 9.8103 | 0 | 0.0510 | 0.1709 | 0.2401 | 0.1810 | 0.3580 |
| 0.60 | 2.9603 | 0.2790 | -0.0739 | -1.7181 | 0.3604 | 9.7820 | 0 | 0.0355 | 0.1677 | 0.2644 | 0.1845 | 0.3739 |
| 0.70 | 2.9058 | 0.2249 | -0.0900 | -1.7493 | 0.4288 | 10.0439 | 0 | 0.0327 | 0.1803 | 0.2704 | 0.1917 | 0.3823 |
| 0.80 | 2.9774 | 0.1850 | -0.0791 | -1.8587 | 0.4595 | 11.0579 | 0 | 0.0312 | 0.2003 | 0.2684 | 0.2082 | 0.3795 |
| 0.90 | 2.8355 | 0.2298 | -0.0737 | -1.8216 | 0.4380 | 10.8397 | 0 | 0.0327 | 0.1876 | 0.2714 | 0.1890 | 0.3839 |
| 1.00 | 2.6846 | 0.2892 | -0.0690 | -1.7704 | 0.4082 | 10.7126 | 0 | 0.0193 | 0.1894 | 0.2687 | 0.2071 | 0.3800 |
| 1.25 | 2.5013 | 0.3133 | -0.0692 | -1.7768 | 0.4113 | 10.7505 | 0 | 0.0379 | 0.2424 | 0.2589 | 0.2119 | 0.3859 |
| 1.50 | 2.4435 | 0.3476 | -0.0748 | -1.8420 | 0.4121 | 10.4345 | 0 | 0.0375 | 0.2842 | 0.2453 | 0.2126 | 0.3879 |
| 1.75 | 2.4401 | 0.2886 | -0.0491 | -1.9249 | 0.4383 | 11.1435 | 0 | 0.0269 | 0.3001 | 0.2256 | 0.2131 | 0.3813 |
| 2.00 | 2.4825 | 0.2391 | -0.0738 | -2.0134 | 0.5054 | 11.8535 | 0 | 0.0087 | 0.2702 | 0.2020 | 0.1892 | 0.3688 |

Table 4b.

| T (s) | a | b1 | b2 | c1 | c2 | h | C0 | C1 | C2 | eve | sta |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 0.03 | 3.3202 | -0.1924 | -0.0284 | 1.7826 | 0.2648 | 9.3572 | 0.0000 | 0.2018 | 0.1123 | 0.1949 | 0.1720 | 0.3294 |
| 0.04 | 3.2650 | 0.2970 | -0.0165 | -1.7046 | 0.1784 | 8.2287 | 0.0000 | 0.2374 | 0.1190 | 0.1884 | 0.1805 | 0.3440 |
| 0.07 | 3.3909 | 0.3814 | -0.0100 | -1.6577 | 0.1074 | 8.1178 | 0.0000 | 0.2120 | 0.1143 | 0.2110 | 0.2179 | 0.3567 |
| 0.10 | 3.4366 | 0.4100 | -0.0181 | -1.6241 | 0.1054 | 8.7309 | 0.0000 | 0.1643 | 0.0928 | 0.2060 | 0.2141 | 0.3483 |
| 0.15 | 3.3749 | 0.4240 | -0.0529 | -1.5927 | 0.1479 | 9.4787 | 0.0000 | 0.1809 | 0.1138 | 0.2010 | 0.2236 | 0.3398 |
| 0.20 | 3.5002 | 0.3262 | -0.0581 | -1.7138 | 0.2297 | 10.2023 | 0.0000 | 0.1455 | 0.1361 | 0.2077 | 0.2138 | 0.3510 |
| 0.25 | 3.3275 | 0.3397 | -0.0703 | -1.6639 | 0.2480 | 9.4903 | 0.0000 | 0.1370 | 0.1388 | 0.2020 | 0.1923 | 0.3414 |
| 0.30 | 3.2208 | 0.3400 | -0.0606 | -1.6390 | 0.2549 | 8.9227 | 0.0000 | 0.0841 | 0.1283 | 0.1994 | 0.1746 | 0.3371 |
| 0.35 | 3.1402 | 0.3360 | -0.0652 | -1.6276 | 0.2657 | 9.1613 | 0.0000 | 0.0896 | 0.1381 | 0.2101 | 0.1707 | 0.3322 |
| 0.40 | 3.0654 | 0.3422 | -0.0663 | -1.6348 | 0.2777 | 9.0618 | 0.0000 | 0.0845 | 0.1570 | 0.2363 | 0.1578 | 0.3522 |
| 0.45 | 3.0478 | 0.3385 | -0.0720 | -1.6634 | 0.3036 | 9.3435 | 0.0000 | 0.0521 | 0.1693 | 0.2446 | 0.1645 | 0.3646 |
| 0.50 | 3.0676 | 0.3488 | -0.0678 | -1.7137 | 0.3060 | 9.9299 | 0.0000 | 0.0552 | 0.1688 | 0.2441 | 0.1833 | 0.3638 |
| 0.60 | 2.9571 | 0.3398 | -0.0473 | -1.7150 | 0.3224 | 9.9319 | 0.0000 | 0.0396 | 0.1656 | 0.2684 | 0.1867 | 0.3795 |
| 0.70 | 2.9166 | 0.2670 | -0.0694 | -1.7539 | 0.4055 | 10.2881 | 0.0000 | 0.0363 | 0.1778 | 0.2739 | 0.1938 | 0.3874 |
| 0.80 | 2.9909 | 0.2220 | -0.0587 | -1.8641 | 0.4399 | 11.3384 | 0.0000 | 0.0347 | 0.1974 | 0.2721 | 0.1910 | 0.3849 |
| 0.90 | 2.8642 | 0.2626 | -0.0525 | -1.8358 | 0.4202 | 11.2612 | 0.0000 | 0.0363 | 0.1847 | 0.2754 | 0.1915 | 0.3894 |
| 1.00 | 2.7167 | 0.3195 | -0.0472 | -1.7865 | 0.3915 | 11.1822 | 0.0000 | 0.0230 | 0.1865 | 0.2725 | 0.2102 | 0.3853 |
| 1.25 | 2.5220 | 0.3241 | -0.0502 | -1.7862 | 0.4095 | 11.1357 | 0.0000 | 0.0426 | 0.2394 | 0.2634 | 0.2159 | 0.3926 |
| 1.50 | 2.4439 | 0.3593 | -0.0551 | -1.8405 | 0.4119 | 10.6114 | 0.0000 | 0.0422 | 0.2804 | 0.2281 | 0.2175 | 0.3855 |
| 1.75 | 2.4238 | 0.3053 | -0.0281 | -1.9148 | 0.4353 | 11.1738 | 0.0000 | 0.0321 | 0.2978 | 0.2300 | 0.1970 | 0.3887 |
| 2.00 | 2.4513 | 0.2559 | -0.0575 | -1.9949 | 0.5060 | 11.7562 | 0.0000 | 0.0147 | 0.2684 | 0.2059 | 0.1932 | 0.3760 |

Table 5

| Study | Parameter | Region | Nrec, Neve | Component | Mrange | M | Rmin, Rmax | Dist_type | Site class |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Akkar and Bommer (2007) | PGV | Europe/Middle East | 532, 131 | L, G | 5-7.6 | Mw | 5-100 | RJB | 3 |
| Ambraseys et al. (2005) | PGA, Resp. spectra | Europe/Middle East | 595, 135 | L | 6-7.6 | Mw | 0-100 | RJB | 4 |
| Boore and Atkinsons (2008) | PGA, PGV, Resp. spectra | Worldwide | 1574, 58 | GMRot | 5-8 | Mw | 0-200 | RJB | Vs,30 |
| Sabetta and Pugliese (1987, 1996) | PGA, PGV, Resp. spectra | Italy | 95, 17 | L | 4.6 – 6.8 | Ml Ms | < 100 | RJB | 3 |

Nella sabetta dobbiamo mettere che hanno sviluppato I modelli anche per altre distanze? Circa le compomenti, dobbiamo indicare quali modelli sono disponibili anche per la verticale?