NATIONAL ANTARCTIC RESEARCH PROGRAM

# Terra Nova Bay, Antarctica

# Geomagnetic Observatory

# Magnetic Observation Results

1998-1999

- Cafarella, S. Lepidi, A. Meloni, P. Palangio, L. Santarelli

2002

# Geomagnetic Observation Results 1998-1999

Terra Nova Bay - Antarctica

# L.  Cafarella, S. Lepidi, A. Meloni, P. Palangio, L. Santarelli

# Istituto Nazionale di Geofisica e Vulcanologia

# Introduction

This report deals with activities undertaken at the Antarctic Italian Geomagnetic Observatory during the austral summer 1998-1999.

The coordinates of the Observatory are the following:

# Geographic latitude: 74.69(S

Geographic longitude: 164.12(E

Magnetic latitude (IGRF95): 77.27(S

Magnetic longitude (IGRF95): 278.60(E

This report describes the activities performed from December 6, 1998 to February 12, 1999.

Beside the fluxgate magnetometer EDA used for the previous yearbooks two more fluxgate magnetometers were operating: RCM (a biaxial ring-core-magnetometer for the horizontal H and D components) and FGE (for H, D and Z components). A comparison of the H and D data from the  operating variometers has shown that the RCM measurements are the most reliable, so for the present work the H and D components from RCM and the Z component from the FGE have been used.

The proton precession magnetometers used to record F total values were Overhauser type; for a  description of instruments we refer to geomagnetism text books, for example Parkinson (1983) and Wienert (1970).

Since the total intensity F time variations, at polar latitudes, where values of inclination is almost 90(, are very close to the vertical component Z time variations, the plots of total intensity time variations are not shown. They can however be obtained from the well known equation:

# F2=H2+Z2

# Absolute measurements

For the normal absolute measurements-taking at the Observatory, a standard fluxgate magnetometer theodolite for the determination of D, I angles has been used; please refer to previous reports for details.

The peak of Cape Washington was used, as azimuth mark, for the computation of the Declination. The geographic coordinates of two geodetic points (Cape Washington and measuring location) were established on the basis of GPS measurements; from these coordinates, an azimuth Az = 82( 37.5’ was found for the measuring point. The proton magnetometer recordings, continuously undertaken during the execution of the DI measurements, have allowed the calculation of the absolute intensive elements.

Table 1 shows absolute measurement values for each element; the values of the intensive components H and Z (rounded off to the nT) were computed using the relations:

# H = F(cos I

# Z = F(sin I

# H0 and D0 reference values computation

All data have been reduced to universal time, using the relation: UT(h) = LT (h) – 13h.

Since the fluxgate was magnetically oriented in the horizontal plane, as in the previous installations, it was necessary to compute H0 and D0 reference values, comparing absolute and relative measurements, at the same time. For the Z component, once the vertical levelling of the sensor was assured, it was assumed that the variations measured by fluxgate were actually the vertical component of the geomagnetic field variations.

In the description the mathematical procedure used for computation of H0 and D0, the following symbols are used:

H0, D0					Reference values

Habs, Dabs				Values of absolute measurements at time t

x,y					Instantaneous variations recorded by fluxgate system at time t

For each absolute measurement, the reference values were computed as:

H0 = Habs( cos(() - x

D0 = Dabs - (

where

(= arcsin (y/Habs)

In order to reduce this dispersion in the set, the Chauvenet criterion was used. The method, based on the hypothesis of a Gauss probability distribution for the data, consists in the elimination of measurements whose difference from the average is greater than a multiple of the standard deviation fixed by the sample dimension (in this case a value 2.74 σ, corresponding to a sample of 79 data elements, was used). This method, however, cannot be applied more than once, since an iterative procedure could exclude most of the values up to the complete elimination of the data (Worthing and Jeffner, 1943).

The average values of H0 and  D0 are:

# H0 = (7706(8) nT

# D0 = (137.76(0.07) deg

## These values are considerably different from those reported in the previous yearbooks because a different instrument was used for the measurements of the instantaneous variations (please refer to the Introduction for more details).

## Daily base lines computation

After H0 and D0 reference values are found, the computation of the base lines in relation to absolute measurements and then the computation of the daily base lines for all days, can follow. The available data are the H, D and Z magnetic element variations recorded by fluxgate system (sampling rate 1 minute) and the absolute measurements recorded from Dec 6, 1998, to Feb 12, 1999.

The base lines computation was undertaken by two different procedures. In the case of Z, assuming that the fluxgate recordings show the variations of the vertical components, the base line (BZ) was computed as the difference between the absolute measurements (Zabs) and the fluxgate measurements (z). On the other hand, in the case of H and D, the magnetic orientation of the fluxgate system axes was taken into account. Using H0 and D0 reference values, the H and D base lines were computed for each absolute measurement as:

BH = Habs – [(H0+x) 2 + y2]1/2

BD = Dabs – D0 – arctg[y/(x+ H0)]

Mean daily values of the base lines were obtained for those days in which more than one absolute measurement was available.

In order to have a daily base line for each magnetic element, a linear regression analysis using the least squares method has been undertaken. The results are shown in Fig. 1, where the experimental data, as well as the best fit lines are reported.

Using the daily base lines, one minute values for the three field elements H, D and Z were computed as:

H = [(H0+x) 2 + y2]1/2 + BH

D = D0 + arctg[y/(x+ H0)] + BD

Z = z + BZ

In Tables 2, 3, 4 all the hourly and daily averages and the total mean values for the H, D and Z elements on the entire measuring period (from Dec 6, 1998 to Feb 12, 1999) are reported; the relative plots are shown in Fig. 2. The plots of the one minute data follow in succession.

# References

Azzara R., E. Bozzo, G. Caneva, A. Meloni and G. Romeo, 1989, Geomagnetic Observation results 1986-1987, National Antarctic Research Program, PNRA, 78p.

Azzara R., E. Bozzo, G. Caneva, A. Meloni and G. Romeo, 1990, Geomagnetic Observation results 1987-1988, National Antarctic Research Program, PNRA, 80p.

Azzara R., E. Bozzo, G. Caneva, A. Meloni and G. Romeo, 1991,Geomagnetic Observation results 1988-1989, National Antarctic Research Program, PNRA, 52p.

Bozzo E., G. Caneva, A. Meloni, P. Palangio, B. Palombo, L. Perrone and G. Romeo, 1992, Geomagnetic Observation results 1989-1990, National Antarctic Research Program, PNRA, 79p.

Bozzo E., G. Caneva, A. Meloni, P. Palangio, L. Perrone and G. Romeo, 1994, Geomagnetic Observation results 1990-1991, Terra Nova Bay - Antarctica, Terra Antarctica, Vol. 1, 185-217.

Bozzo E., L. Cafarella, G. Caneva, C. Falcone, A. Meloni, P. Palangio and A. Zirizzotti, 1995, Geomagnetic Observation results 1991-1992/1992-1993, National Antarctic Research Program, PNRA, 54p.

Bozzo E., L. Cafarella, G. Caneva, A. Meloni, P. Palangio and A. Zirizzotti, 1996, Geomagnetic Observation results 1993-1994, National Antarctic Research Program, PNRA, 71p.

Cafarella L., S. Lepidi, A. Meloni and P. Palangio, 1997, Geomagnetic Observation results 1994-1995, National Antarctic Research Program, PNRA, 58p.

Parkinson, W.D., 1983. Introduction to Geomagnetism. Scottish Academic Press. Edinburgh, London, 433 pp.

Wienert, K.A., 1970. Notes on Geomagnetic Observatory and survey practice; Unesco, Parigi.

Worthing, A. G., Jeffner J., 1943. Treatment of experimental data, John Wiley, New York.

#### Table captions

# Table 1: Absolute measurement values 1998/1999

# Table 2: Horizontal intensity hourly and daily means

(from Dec 6, 1998 to Feb 12, 1999)

# Table 3: Declination hourly and daily means

(from Dec 6, 1998 to Feb 12, 1999)

# Table 4: Vertical intensity hourly and daily means

(from Dec 6, 1998 to Feb 12, 1999)

#### Figure Captions

# Fig 1: Scatter plot and linear regression for daily H, D and Z base lines.

# Fig 2: Hourly means of the H, D and Z1 elements during the whole campaign.

# Figg. 3 – 69: Daily plots of the one minute values of the H, D and Z1 elements.

# Footnotes

Z values must be considered negative